## Slide 1: SETG 2363 Strength of Materials Stress
Mohsin Mohd Sies
Nuclear Engineering,
Faculty of Chemical and Energy Engineering,
Universiti Teknologi Malaysia

## Slide 2: CHAPTER OBJECTIVES
Use the principles to determine internal resultant loadings in a body
Introduce concepts of normal and shear stress
Discuss applications of analysis and design of members subjected to an axial load or direct shear

## Slide 3: CHAPTER OUTLINE
Introduction
Equilibrium of a deformable body
Stress
Average normal stress in an axially loaded bar
Average shear stress
Allowable stress
Design of simple connections

## Slide 4: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Internal resultant loadings
For coplanar (2D) loadings:
  Normal force, N
  Shear force, V
  Bending moment, M

## Slide 5: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Internal resultant loadings
For coplanar loadings:
  Apply ∑ Fx = 0 to solve for N
  Apply ∑ Fy = 0 to solve for V
  Apply ∑ MO = 0 to solve for M

## Slide 6: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for Analysis
Method of sections
  Choose segment to analyze
  Determine Support Reactions
  Draw free-body diagram for whole body
  Apply equations of equilibrium

## Slide 7: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for analysis
Free-body diagram
  Keep all external loadings in exact locations before “sectioning”
  Indicate unknown resultants, N, V, M, and T at the section, normally at centroid C of sectioned area
  Coplanar system of forces only include N, V, and M
  Establish x, y, z coordinate axes with origin at centroid

## Slide 8: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for analysis
Equations of equilibrium
  Sum moments at section, about each coordinate axes where resultants act
  This will eliminate unknown forces N and V, with direct solution for M (and T)
  Resultant force with negative value implies that assumed direction is opposite to that shown on free-body diagram

## Slide 9: EXAMPLE 1.1
Determine resultant loadings acting on cross section at C of beam.

## Slide 10: EXAMPLE 1.1 (SOLN)
Support Reactions
Consider segment CB
Free-Body Diagram:
Keep distributed loading exactly where it is on segment CB after “cutting” the section.
Replace it with a single resultant force, F.

## Slide 11
for a triangular distributed load — also called a uniformly varying load— the magnitude of the equivalent force is the area of the triangle, 1/2(L.h) and the line of action passes through the centroid of the triangle. The horizontal distance from the larger end of the triangle to the centroid is (1/3)L.

## Slide 12: EXAMPLE 1.1 (SOLN)
Intensity (w) of loading at C (by proportion)
w/6 m = (270 N/m)/9 m
w = 180 N/m
F = ½ (180 N/m)(6 m) = 540 N (area of triangle)
F acts 1/3(6 m) = 2 m from C.
Free-Body Diagram:

## Slide 13: EXAMPLE 1.1 (SOLN)
Equilibrium equations:
∑ Fx = 0;
∑ Fy = 0;
∑ Mc = 0;
− Nc = 0
Nc = 0
Vc − 540 N = 0
Vc = 540 N
−Mc − 504 N (2 m) = 0
Mc = −1080 N·m
+
+
+
Negative sign of Mc means it acts in the opposite direction to that shown

## Slide 14: Review of Statics
The structure is designed to support a 30 kN load
Perform a static analysis to determine the internal force in each structural member and the reaction forces at the supports
The structure consists of a beam and rod joined by pins (zero moment connections) at the junctions and supports

## Slide 15: Structure Free-Body Diagram
Structure is detached from supports and the loads and reaction forces are indicated
Ay and Cy can not be determined from these equations
Conditions for static equilibrium:

## Slide 16: Component Free-Body Diagram
In addition to the complete structure, each component must satisfy the conditions for static equilibrium
Results:
Reaction forces are directed along boom and rod
Consider a free-body diagram of the boom;
substitute into the structure equilibrium equation

## Slide 17: Method of Joints
The boom and rod are 2-force members, i.e., the members are subjected to only two forces which are applied at member ends
Joints must satisfy the conditions for static equilibrium which may be expressed in the form of a force triangle:
For equilibrium, the forces must be parallel to to an axis between the force application points, equal in magnitude, and in opposite directions

## Slide 18: Stress Analysis
Conclusion: the strength of member BC is adequate
From the material properties for steel, the allowable stress is
Can the structure safely support the 30 kN load?
At any section through member BC, the internal force is 50 kN with a force intensity or stress of
dBC = 20 mm
From a statics analysis
FAB = 40 kN (compression)
FBC = 50 kN (tension)

## Slide 21: 1.3 STRESS
Concept of stress
To obtain distribution of force acting over a sectioned area
Assumptions of material:
  It is continuous (uniform distribution of matter)
  It is cohesive (all portions are connected together)

## Slide 22: 1.3 STRESS
Concept of stress
Consider ΔA in figure below
Small finite force, ΔF acts on ΔA

## Slide 23: 1.3 STRESS
Normal stress
Intensity of force, or force per unit area, acting normal to ΔA
Symbol used for normal stress, is σ (sigma)
Tensile stress: normal force “pulls” or “stretches” the area element ΔA
Compressive stress: normal force “pushes” or “compresses” area element ΔA
σz =
lim
ΔA →0
ΔFz
ΔA

## Slide 24: 1.3 STRESS
Normal stress

## Slide 25: 1.3 STRESS
Shear stress
Intensity of force, or force per unit area, acting tangent to ΔA
Symbol used for shear stress is τ (tau)
τzx =
lim
ΔA →0
ΔFx
ΔA
τzy =
lim
ΔA →0
ΔFy
ΔA

## Slide 26: 1.3 STRESS
Shear stress

## Slide 27
Beer • Johnston • DeWolf
Stress-Strain Test

## Slide 28
Beer • Johnston • DeWolf
Stress-Strain Diagram: Ductile Materials

## Slide 29
Beer • Johnston • DeWolf
Stress-Strain Diagram: Brittle Materials

## Slide 30
Beer • Johnston • DeWolf
Hooke’s Law: Modulus of Elasticity
Below the yield stress
  E
E  Youngs Modulus or Modulus of Elasticity
Strength is affected by alloying, heat treating, and manufacturing process but stiffness (Modulus of Elasticity) is not.

## Slide 31
Beer • Johnston • DeWolf
Elastic vs. Plastic Behavior
If the strain disappears when the stress is removed, the material is said to behave elastically.
When the strain does not return to zero after the stress is removed, the material is said to behave plastically.
The largest stress for which this occurs is called the elastic limit.

## Slide 32
Beer • Johnston • DeWolf
Strength vs. Stiffness vs. Hardness
Strength
A material's ability to resist deformation or fracture when stress is applied. Strength is measured by tensile strength, which is the stress a material can withstand before breaking, and yield strength, which is the stress a material can withstand before permanently deforming.
Stiffness
A material's ability to return to its original shape after being deformed by an applied force. Stiffness is also known as the modulus of elasticity.
Hardness
A material's resistance to surface deformation, wear, tear, scratching, and abrasion. Some examples of hard materials include diamond, boron carbide, quartz, tempered steel, ice, granite, and concrete.
In general, stronger materials are also stiffer and harder. For example, in some metals, like steel, hardness and tensile strength are roughly proportional. However, it's important to note that while there is often a correlation between strength and stiffness, the two terms should be clearly separated for manufacturing purposes.

## Slide 33
Beer • Johnston • DeWolf
Strength
Yield strength is used to describe materials that exhibit elastic behavior. It’s the maximum tensile stress the material can handle before permanent deformation.
Ultimate strength refers to the maximum stress before failure occurs.
Fracture strength is the value corresponding to the stress at which total failure occurs.
Strength is also represented by the total area under the stress-strain curve

## Slide 37: Photoelastic Stress Analysis

## Slide 38: Photoelastic Stress Analysis

## Slide 41: Prismatic bar
A prismatic bar or beam is a straight structural piece that has the same cross-section throughout its length

## Slide 42: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Examples of axially loaded bar
Usually long and slender structural members
Truss members, hangers, bolts
Prismatic means all the cross sections are the same

## Slide 43: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Assumptions
Uniform deformation: Bar remains straight before and after load is applied, and cross section remains flat or plane during deformation
In order for uniform deformation, force P be applied along centroidal axis of cross section

## Slide 44: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Average normal stress distribution
σ = average normal stress at any point on cross sectional area
P = internal resultant normal force
A = x-sectional area of the bar
FRz = ∑ Fxz
∫ dF = ∫A σ dA
P = σ A
+
P
A
σ =

## Slide 45: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Equilibrium
Consider vertical equilibrium of the element
When the bar is stretched by the force P, the resulting stresses are tensile stresses
If the force P cause the bar to be compressed, we obtain compressive stresses

## Slide 46: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Sign convention for normal stresses is:
    (+) for tensile stresses and
    (-) for compressive stresses
Because the normal stress σ is obtained by dividing the axial force by the cross–sectional area, it has units of force per unit of area.
In SI units:
Force is expressed in newtons (N) and area in square meters (m2). A N/m2 is a pascals (Pa).

## Slide 47: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Maximum average normal stress
For problems where internal force P and x-sectional A were constant along the longitudinal axis of the bar, normal stress σ = P/A is also constant
If the bar is subjected to several external loads along its axis, change in x-sectional area may occur
Thus, it is important to find the maximum average normal stress
To determine that, we need to find the location where ratio P/A is a maximum

## Slide 48: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Maximum average normal stress
Draw an axial or normal force diagram (plot of P vs. its position x along bar’s length)
Sign convention:
  P is positive (+) if it causes tension in the member
  P is negative (−) if it causes compression
Identify the maximum average normal stress from the plot

## Slide 49: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for Analysis
Average normal stress
Use equation of σ = P/A for x-sectional area of a member when section subjected to internal resultant force P

## Slide 50: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for Analysis
Axially loaded members
Internal Loading:
Section member perpendicular to its longitudinal axis at point where normal stress is to be determined
Draw free-body diagram
Use equation of force equilibrium to obtain internal axial force P at the section

## Slide 51: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for Analysis
Axially loaded members
Average Normal Stress:
Determine member’s x-sectional area at the section
Compute average normal stress σ = P/A

## Slide 52: EXAMPLE 1.6
Bar width = 35 mm, thickness = 10 mm
Determine max. average normal stress in bar when subjected to loading shown.

## Slide 53: EXAMPLE 1.6 (SOLN)
Internal loading
Normal force diagram
By inspection, largest loading area is BC, where PBC = 30 kN

## Slide 54: EXAMPLE 1.6 (SOLN)
Average normal stress
σBC =
PBC
A
30(103) N
(0.035 m)(0.010 m)
=
= 85.7 MPa

## Slide 57: 1.5 AVERAGE SHEAR STRESS
Shear stress is the stress component that act in the plane of the sectioned area.
Consider a force F acting to the bar
For rigid supports, and F is large enough, bar will deform and fail along the planes identified by AB and CD
Free-body diagram indicates that shear force, V = F/2 be applied at both sections to ensure equilibrium

## Slide 58: 1.5 AVERAGE SHEAR STRESS
Average shear stress over each section is:
τavg = average shear stress at section, assumed to be same at each pt on the section
V = internal resultant shear force at section determined from equations of equilibrium
A = area of section
P
A
τavg =

## Slide 59: 1.5 AVERAGE SHEAR STRESS
Case discussed above is example of simple or direct shear
Caused by the direct action of applied load F
Occurs in various types of simple connections, e.g., bolts, pins, welded material

## Slide 62: 1.5 AVERAGE SHEAR STRESS
Single shear
Steel and wood joints shown below are examples of single-shear connections, also known as lap joints.
Since we assume members are thin, there are no moments caused by F

## Slide 63: 1.5 AVERAGE SHEAR STRESS
Single shear
For equilibrium, x-sectional area of bolt and bonding surface between the two members are subjected to single shear force, V = F
The average shear stress equation can be applied to determine average shear stress acting on colored section in (d).

## Slide 64: 1.5 AVERAGE SHEAR STRESS
Double shear
The joints shown below are examples of double-shear connections, often called double lap joints.
For equilibrium, x-sectional area of bolt and bonding surface between two members subjected to double shear force, V = F/2
Apply average shear stress equation to determine average shear stress acting on colored section in (d).

## Slide 65: Shearing Stress Examples
Single Shear
Double Shear

## Slide 68: 1.5 AVERAGE SHEAR STRESS
Procedure for analysis
Internal shear
Section member at the point where the τavg is to be determined
Draw free-body diagram
Calculate the internal shear force V
Average shear stress
Determine sectioned area A
Compute average shear stress τavg = V/A

## Slide 69: EXAMPLE 1.10
Depth and thickness = 40 mm
Determine average normal stress and average shear stress acting along (a) section planes a-a, and (b) section plane b-b.

## Slide 70: EXAMPLE 1.10 (SOLN)
Part (a)
Internal loading
Based on free-body diagram, Resultant loading of axial force, P = 800 N

## Slide 71: EXAMPLE 1.10 (SOLN)
Part (a)
Average stress
Average normal stress, σ
σ =
P
A
800 N
(0.04 m)(0.04 m)
= 500 kPa
=

## Slide 72: EXAMPLE 1.10 (SOLN)
Part (a)
Internal loading
No shear stress on section, since shear force at section is zero.
τavg = 0

## Slide 73: EXAMPLE 1.10 (SOLN)
Part (b)
Internal loading
+
∑ Fx = 0;
− 800 N + N sin 60° + V cos 60° = 0
+
∑ Fy = 0;
V sin 60° − N cos 60° = 0

## Slide 74: EXAMPLE 1.10 (SOLN)
Part (b)
Internal loading
Or directly using x’, y’ axes,
∑ Fx’ = 0;
∑ Fy’ = 0;
+
+
N − 800 N cos 30° = 0
V − 800 N sin 30° = 0

## Slide 75: EXAMPLE 1.10 (SOLN)
Part (b)
Average normal stress
σ =
N
A
692.8 N
(0.04 m)(0.04 m/sin 60°)
= 375 kPa
=

## Slide 76: EXAMPLE 1.10 (SOLN)
Part (b)
Average shear stress
τavg =
V
A
400 N
(0.04 m)(0.04 m/sin 60°)
= 217 kPa
=
Stress distribution shown below

## Slide 77: EXAMPLE 1.11 (SOLN)

## Slide 78: EXAMPLE 1.11 (SOLN)

## Slide 79: Bearing Stress in Connections
Bolts, rivets, and pins create stresses on the points of contact or bearing surfaces of the members they connect.
Corresponding average force intensity is called the bearing stress,
The resultant of the force distribution on the surface is equal and opposite to the force exerted on the pin.

## Slide 80: Pin Bearing Stresses
To determine the bearing stress at A in the boom AB, we have t = 30 mm and d = 25 mm,
To determine the bearing stress at A in the bracket, we have t = 2(25 mm) = 50 mm and d = 25 mm,

## Slide 81: 1.6 ALLOWABLE STRESS
Factor of safety considerations:
uncertainty in material properties
uncertainty of loadings, number of loading cycles
uncertainty of analyses
types of failure
maintenance requirements and deterioration effects
importance of member to structures integrity
risk to life and property, influence on machine function

## Slide 82: 1.6 ALLOWABLE STRESS
When designing a structural member or mechanical element, the stress in it must be restricted to safe level
Choose an allowable load that is less than the load the member can fully support
One method used is the factor of safety (F.S.)
F.S. =
Ffail
Fallow

## Slide 83: 1.6 ALLOWABLE STRESS
If load applied is linearly related to stress developed within member, then F.S. can also be expressed as:
F.S. =
σfail
σallow
F.S. =
τfail
τallow
In all the equations, F.S. is chosen to be greater than 1, to avoid potential for failure.
Specific values will depend on types of material used and its intended purpose.

## Slide 84: 1.7 DESIGN OF SIMPLE CONNECTIONS
To determine area of section subjected to a normal force, use
A =
P
σallow
A =
V
τallow
To determine area of section subjected to a shear force, use

## Slide 85: 1.7 DESIGN OF SIMPLE CONNECTIONS
Cross-sectional area of a tension member
Condition:
The force has a line of action that passes through the centroid of the cross section.

## Slide 86: 1.7 DESIGN OF SIMPLE CONNECTIONS
Cross-sectional area of a connecter subjected to shear
Assumption:
If bolt is loose or clamping force of bolt is unknown, assume frictional force between plates to be negligible.

## Slide 87: 1.7 DESIGN OF SIMPLE CONNECTIONS
Assumptions:
(σb)allow of concrete < (σb)allow of base plate
Bearing stress is uniformly distributed between plate and concrete
Required area to resist bearing
Bearing stress is normal stress produced by the compression of one surface against another.

## Slide 88: 1.7 DESIGN OF SIMPLE CONNECTIONS
Although actual shear-stress distribution along rod difficult to determine, we assume it is uniform.
Thus use A = V / τallow to calculate l, provided d and τallow is known.
Required area to resist shear caused by axial load

## Slide 89: 1.7 DESIGN OF SIMPLE CONNECTIONS
Procedure for analysis
When using average normal stress and shear stress equations, consider first the section over which the critical stress is acting
Internal Loading
  Section member through x-sectional area
  Draw a free-body diagram of segment of member
  Use equations of equilibrium to determine internal resultant force

## Slide 90: 1.7 DESIGN OF SIMPLE CONNECTIONS
Procedure for Analysis
Required Area
Based on known allowable stress, calculate required area needed to sustain load from A = P/τallow or A = V/τallow

## Slide 91: EXAMPLE 1.13
The two members pinned together at B. If the pins have an allowable shear stress of τallow = 90 MPa, and allowable tensile stress of rod CB is (σt)allow = 115 MPa
Determine to nearest mm the smallest diameter of pins A and B and the diameter of rod CB necessary to support the load.

## Slide 92: EXAMPLE 1.13 (SOLN)
Draw free-body diagram:

## Slide 93: EXAMPLE 1.13 (SOLN)
Diameter of pins:
dA = 6.3 mm
AA =
VA
Tallow
2.84 kN
90  103 kPa
=
= 31.56  10−6 m2 = (dA2/4)
dB = 9.7 mm
AB =
VB
Tallow
6.67 kN
90  103 kPa
=
= 74.11  10−6 m2 = (dB2/4)

## Slide 94: EXAMPLE 1.13 (SOLN)
Diameter of pins:
dA = 7 mm
dB = 10 mm
Choose a size larger to nearest millimeter.

## Slide 95: EXAMPLE 1.13 (SOLN)
Diameter of rod:
dBC = 8.59 mm
ABC =
P
(σt)allow
6.67 kN
115  103 kPa
=
= 58  10−6 m2 = (dBC2/4)
dBC = 9 mm
Choose a size larger to nearest millimeter.

## Slide 110: CHAPTER REVIEW
Internal loadings consist of
  Normal force, N
  Shear force, V
  Bending moments, M
  Torsional moments, T
Get the resultants using
  method of sections
  Equations of equilibrium

## Slide 111: CHAPTER REVIEW
Assumptions for a uniform normal stress distribution over x-section of member (σ = P/A)
  Member made from homogeneous isotropic material
  Subjected to a series of external axial loads that,
  The loads must pass through centroid of cross-section

## Slide 112: CHAPTER REVIEW
Determine average shear stress by using τ = V/A equation
  V is the resultant shear force on cross-sectional area A
  Formula is used mostly to find average shear stress in fasteners or in parts for connections

## Slide 113: CHAPTER REVIEW
Design of any simple connection requires that
  Average stress along any cross-section not exceed a factor of safety (F.S.) or
  Allowable value of σallow or τallow
  These values are reported in codes or standards and are deemed safe on basis of experiments or through experience