## Slide 1: SETG 2363 Strength of Materials Stress Transformation
Mohsin Mohd Sies
Nuclear Engineering,
Faculty of Chemical and Energy Engineering,
Universiti Teknologi Malaysia

## Slide 2: CHAPTER OBJECTIVES
Derive equations for transforming stress components between coordinate systems of different orientation
Use derived equations to obtain the maximum normal and maximum shear stress at a point
Determine the orientation of elements upon which the maximum normal and maximum shear stress acts

## Slide 3: CHAPTER OBJECTIVES
Discuss a method for determining the absolute maximum shear stress at a point when material is subjected to plane and 3-dimensional states of stress

## Slide 4: CHAPTER OUTLINE
Plane-Stress Transformation
General Equations of Plane Stress Transformation
Principal Stresses and Maximum In-Plane Shear Stress
Mohr’s Circle – Plane Stress
Stress in Shafts Due to Axial Load and Torsion
Stress Variations Throughout a Prismatic Beam
Absolute Maximum Shear Stress

## Slide 5: 9.1 PLANE-STRESS TRANSFORMATION
General state of stress at a pt is characterized by six independent normal and shear stress components.
In practice, approximations and simplifications are done to reduce the stress components to a single plane.

## Slide 6: 9.1 PLANE-STRESS TRANSFORMATION
The material is then said to be subjected to plane stress.
For general state of plane stress at a pt, we represent it via normal-stress components, x, y and shear-stress component xy.
Thus, state of plane stress at the pt is uniquely represented by three components acting on an element that has a specific orientation at that pt.

## Slide 7: 9.1 PLANE-STRESS TRANSFORMATION
The most general state of stress at a point may be represented by 6 components,
Same state of stress is represented by a different set of components if axes are rotated.

## Slide 8: 9.1 PLANE-STRESS TRANSFORMATION
Transforming stress components from one orientation to the other is similar in concept to how we transform force components from one system of axes to the other.
Note that for stress-component transformation, we need to account for
  the magnitude and direction of each stress component, and
  the orientation of the area upon which each component acts.

## Slide 9: 9.1 PLANE-STRESS TRANSFORMATION
Procedure for Analysis
If state of stress at a pt is known for a given orientation of an element of material, then state of stress for another orientation can be determined
=

## Slide 10: 9.1 PLANE-STRESS TRANSFORMATION
Procedure for Analysis
Section element as shown.
Assume that the sectioned area is ∆A, then adjacent areas of the segment will be ∆A sin and ∆A cos.
Draw free-body diagram of segment, showing the forces that act on the element. (Tip: Multiply stress components on each face by the area upon which they act)

## Slide 11: 9.1 PLANE-STRESS TRANSFORMATION
Procedure for Analysis
Apply equations of force equilibrium in the x’ and y’ directions to obtain the two unknown stress components x’, and x’y’.
To determine y’ (that acts on the +y’ face of the element), consider a segment of element shown below.
Follow the same procedure as described previously.
Shear stress x’y’ need not be determined as it is complementary.

## Slide 12: EXAMPLE 9.1
State of plane stress at a pt on surface of airplane fuselage is represented on the element oriented as shown. Represent the state of stress at the pt that is oriented 30 clockwise from the position shown.

## Slide 13: EXAMPLE 9.1 (SOLN)
CASE A (a-a section)
Section element by line a-a and remove bottom segment.
Assume sectioned (inclined) plane has an area of ∆A, horizontal and vertical planes have area as shown.
Free-body diagram of segment is also shown.

## Slide 14: EXAMPLE 9.1 (SOLN)
Apply equations of force equilibrium in the x’ and y’ directions (to avoid simultaneous solution for the two unknowns)
+ Fx’ = 0;

## Slide 15: EXAMPLE 9.1 (SOLN)
+ Fy’ = 0;
Since x’ is negative, it acts in the opposite direction we initially assumed.

## Slide 16: EXAMPLE 9.1 (SOLN)
CASE B (b-b section)
Repeat the procedure to obtain the stress on the perpendicular plane b-b.
Section element as shown on the upper right.
Orientate the +x’ axis outward, perpendicular to the sectioned face, with the free-body diagram as shown.

## Slide 17: EXAMPLE 9.1 (SOLN)
+ Fx’ = 0;

## Slide 18: EXAMPLE 9.1 (SOLN)
+ Fy’ = 0;
Since x’ is negative, it acts opposite to its direction shown.

## Slide 19: EXAMPLE 9.1 (SOLN)
The transformed stress components are as shown.
From this analysis, we conclude that the state of stress at the pt can be represented by choosing an element oriented as shown in the Case A or by choosing a different orientation in the Case B.
Stated simply, states of stress are equivalent.

## Slide 20: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Sign Convention
We will adopt the same sign convention as discussed in chapter 1.3.
Positive normal stresses, x and y, acts outward from all faces
Positive shear stress xy acts upward on the right-hand face of the element.

## Slide 21: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Sign Convention
The orientation of the inclined plane is determined using the angle .
Establish a positive x’ and y’ axes using the right-hand rule.
Angle  is positive if it moves counterclockwise from the +x axis to the +x’ axis.

## Slide 22: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Normal and shear stress components
Section element as shown.
Assume sectioned area is ∆A.
Free-body diagram of element is shown.

## Slide 23: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Normal and shear stress components
Apply equations of force equilibrium to determine unknown stress components:
+ Fx’ = 0;

## Slide 24: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Normal and shear stress components
+ Fy’ = 0;
Simplify the above two equations using trigonometric identities sin2 = 2 sin cos, sin2 = (1  cos2)/2, and cos2 =(1+cos2)/2.

## Slide 25: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Normal and shear stress components
If y’ is needed, substitute ( =  + 90) for  into Eqn 9-1.

## Slide 26: 9.2 GENERAL EQNS OF PLANE-STRESS TRANSFORMATION
Procedure for Analysis
To apply equations 9-1 and 9-2, just substitute the known data for x, y, xy, and  according to established sign convention.
If x’ and x’y’ are calculated as positive quantities, then these stresses act in the positive direction of the x’ and y’ axes.
Tip: For your convenience, equations 9-1 to 9-3 can be programmed on your pocket calculator.

## Slide 27: EXAMPLE 9.2
State of stress at a point is represented by the element shown. Determine the state of stress at the point on another element orientated 30 clockwise from the position shown.

## Slide 28: EXAMPLE 9.2 (SOLN)
This problem was solved in Example 9.1 using basic principles. Here we apply Eqns. 9-1 and 9-2.
From established sign convention,
Plane CD
+x’ axis is directed outward, perpendicular to CD, and +y’ axis directed along CD.
Angle measured is  = 30 (clockwise).

## Slide 29: EXAMPLE 9.2 (SOLN)
Plane CD
Apply Eqns 9-1 and 9-2:
The negative signs indicate that x’ and x’y’ act in the negative x’ and y’ directions.

## Slide 30: EXAMPLE 9.2 (SOLN)
Plane BC
Similarly, stress components acting on face BC are obtained using  = 60.

## Slide 31: EXAMPLE 9.2 (SOLN)
As shown, shear stress x’y’ was computed twice to provide a check.
Negative sign for x’ indicates that stress acts in the negative x’ direction.
The results are shown below.

## Slide 32: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
In-plane principal stresses
Differentiate Eqn. 9-1 w.r.t.  and equate to zero:
Solving the equation and let  = P, we get
Solution has two roots,  p1, and  p2.
 p1, and  p2 are 90 degrees apart.

## Slide 33: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
In-plane principal stresses
For  p1,
For  p2,

## Slide 34: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
In-plane principal stresses
Substituting either of the two sets of trigonometric relations into Eqn 9-1, we get
The Eqn gives the maximum/minimum in-plane normal stress acting at a pt, where 1  2 .
The values obtained are the principal in-plane principal stresses, and the related planes are the principal planes of stress.

## Slide 35: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
In-plane principal stresses
If the trigonometric relations for p1 and p2 are substituted into Eqn 9-2, it can be seen that x’y’ = 0.
No shear stress acts on the principal planes.
Maximum in-plane shear stress
Differentiate Eqn. 9-2 w.r.t.  and equate to zero:

## Slide 36: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
Maximum in-plane shear stress
The two roots of this equation, s1 and s2 can be determined using the shaded triangles as shown.
The planes for maximum shear stress can be determined by orienting an element 45 from the position of an element that defines the plane of principal stress.

## Slide 37: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
Maximum in-plane shear stress
Using either one of the roots s1 and s2, and taking trigo values of sin 2s and cos 2s and substitute into Eqn 9-2:
Value calculated in Eqn 9-7 is referred to as the maximum in-plane shear stress.

## Slide 38: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
Maximum in-plane shear stress
Substitute values for sin 2s and cos 2s into Eqn 9-1, we get a normal stress acting on the planes of maximum in-plane shear stress:
You can also program the above equations on your pocket calculator.

## Slide 39: 9.2 PRINCIPAL STRESSES AND MAXIMUM IN-PLANE SHEAR STRESS
IMPORTANT
Principal stresses represent the maximum and minimum normal stresses at the pt.
When state of stress is represented by principal stresses, no shear stress will act on element.
State of stress at the pt can also be represented in terms of the maximum in-plane shear stress. An average normal stress will also act on the element.
Element representing the maximum in-plane shear stress with associated average normal stresses is oriented 45 from element represented principal stresses.

## Slide 40: EXAMPLE 9.3
When torsional loading T is applied to bar, it produces a state of pure shear stress in the material. Determine (a) the maximum in-plane shear stress and associated average normal stress, and (b) the principal stress.

## Slide 41: EXAMPLE 9.3 (SOLN)
From established sign convention:
Maximum in-plane shear stress
Apply Eqns 9-7 and 9-8,

## Slide 42: EXAMPLE 9.3 (SOLN)
Maximum in-plane shear stress
As expected, maximum in-plane shear stress represented by element shown initially.
Experimental results show that materials that are ductile will fail due to shear stress. Thus, with a torque applied to a bar made from mild steel, the maximum in-plane shear stress will cause failure as shown.

## Slide 43: EXAMPLE 9.3 (SOLN)
Principal stress
Apply Eqns 9-4 and 9-5,

## Slide 44: EXAMPLE 9.3 (SOLN)
Principal stress
Apply Eqn 9-1 with p2 = 45
Thus, if 2 =  acts at p2 = 45 as shown, and 1 =  acts on the other face, p1 = 135.

## Slide 45: EXAMPLE 9.3 (SOLN)
Principal stress
Materials that are brittle fail due to normal stress. An example is cast iron when subjected to torsion, fails in tension at 45 inclination as shown below.

## Slide 46: EXAMPLE 9.6
State of plane stress at a pt on a body is represented on the element shown. Represent this stress state in terms of the maximum in-plane shear stress and associated average normal stress.

## Slide 47: EXAMPLE 9.6 (SOLN)
Orientation of element
Since x = 20 MPa, y = 90 MPa, and xy = 60 MPa and applying Eqn 9-6,
Note that the angles are 45 away from principal planes of stress.

## Slide 48: EXAMPLE 9.6 (SOLN)
Maximum in-plane shear stress
Applying Eqn 9-7,
Thus acts in the +y’ direction on this face ( = 21.3).

## Slide 49: EXAMPLE 9.6 (SOLN)
Average normal stress
Besides the maximum shear stress, the element is also subjected to an average normal stress determined from Eqn. 9-8:
This is a tensile stress.

## Slide 50: 9.4 MOHR’S CIRCLE: PLANE STRESS
Equations for plane stress transformation have a graphical solution that is easy to remember and use.
This approach will help you to “visualize” how the normal and shear stress components vary as the plane acted on is oriented in different directions.

## Slide 51: 9.4 MOHR’S CIRCLE: PLANE STRESS
If Eqs. (9–1) and (9–2) are written in the following form:
Stress Transformation Equations
Elimination of
By squaring Eqs. (9–9) and (9–10) and adding them together, the parameter is eliminated, yielding:

## Slide 52: 9.4 MOHR’S CIRCLE: PLANE STRESS
Compact Form (Mohr’s Circle Equation)
Since , , and are known constants, the equation can be written in the compact form, which is a parametric equation for a circle :
where the average normal stress is
and the radius of Mohr’s circle is

## Slide 53: 9.4 MOHR’S CIRCLE: PLANE STRESS
Establish coordinate axes;  positive to the right and  positive downward, Eqn 9-11 represents a circle having radius R and center on the  axis at pt C (avg, 0). This is called the Mohr’s Circle.

## Slide 54: 9.4 MOHR’S CIRCLE: PLANE STRESS
To draw the Mohr’s circle, we must establish the  and  axes.
Center of circle C (avg, 0) is plotted from the known stress components (x, y, xy).
We need to know at least one pt on the circle to get the radius of circle.

## Slide 55: 9.4 MOHR’S CIRCLE: PLANE STRESS
Case 1 (x’ axis coincident with x axis)
   = 0
  x’ = x
  x’y’ = xy.
Consider this as reference pt A, and plot its coordinates A (x, xy).
Apply Pythagoras theorem to shaded triangle to determine radius R.
Using pts C and A, the circle can now be drawn.

## Slide 56: 9.4 MOHR’S CIRCLE: PLANE STRESS
Case 2 (x’ axis rotated 90 counterclockwise)
   = 90
  x’ = y
  x’y’ = xy.
Its coordinates are G (y, xy).
Hence radial line CG is 180 counterclockwise from “reference line” CA.

## Slide 58: 9.4 MOHR’S CIRCLE: PLANE STRESS
Key Implications
Maximum shear stress occurs at the top and bottom of the circle.
Principal stresses 1, 2 occur where the circle intersects the -axis.
Physical rotation of the stress element by corresponds to a rotation of on Mohr’s circle.

## Slide 59: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Construction of the circle
Establish coordinate system where abscissa represents the normal stress , (+ve to the right), and the ordinate represents shear stress , (+ve downward).
Use positive sign convention for x, y, xy, plot the center of the circle C, located on the  axis at a distance avg = (x + y)/2 from the origin.

## Slide 60: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Construction of the circle
Plot reference pt A (x, xy). This pt represents the normal and shear stress components on the element’s right-hand vertical face. Since x’ axis coincides with x axis,  = 0.

## Slide 61: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Construction of the circle
Connect pt A with center C of the circle and determine CA by trigonometry. The distance represents the radius R of the circle.
Once R has been determined, sketch the circle.

## Slide 62: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Principal stress
Principal stresses 1 and 2 (1  2) are represented by two pts B and D where the circle intersects the -axis.

## Slide 63: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Principal stress
These stresses act on planes defined by angles p1 and p2. They are represented on the circle by angles 2p1 and 2p2 and measured from radial reference line CA to lines CB and CD respectively.

## Slide 64: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Principal stress
Using trigonometry, only one of these angles needs to be calculated from the circle, since p1 and p2 are 90 apart. Remember that direction of rotation 2p on the circle represents the same direction of rotation p from reference axis (+x) to principal plane (+x’).

## Slide 65: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Maximum in-plane shear stress
The average normal stress and maximum in-plane shear stress components are determined from the circle as the coordinates of either pt E or F.

## Slide 66: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Maximum in-plane shear stress
The angles s1 and s2 give the orientation of the planes that contain these components. The angle 2s can be determined using trigonometry. Here rotation is clockwise, and so s1 must be clockwise on the element.

## Slide 67: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Stresses on arbitrary plane
Normal and shear stress components x’ and x’y’ acting on a specified plane defined by the angle , can be obtained from the circle by using trigonometry to determine the coordinates of pt P.

## Slide 68: 9.4 MOHR’S CIRCLE: PLANE STRESS
Procedure for Analysis
Stresses on arbitrary plane
To locate pt P, known angle  for the plane (in this case counterclockwise) must be measured on the circle in the same direction 2 (counterclockwise), from the radial reference line CA to the radial line CP.

## Slide 69: EXAMPLE 9.9
Due to applied loading, element at pt A on solid cylinder as shown is subjected to the state of stress. Determine the principal stresses acting at this pt.

## Slide 70: EXAMPLE 9.9 (SOLN)
Construction of the circle
Center of the circle is at
Initial pt A (2, 6) and the center C (6, 0) are plotted as shown. The circle having a radius of

## Slide 71: EXAMPLE 9.9 (SOLN)
Principal stresses
Principal stresses indicated at pts B and D. For 1 > 2,
Obtain orientation of element by calculating counterclockwise angle 2p2, which defines the direction of p2 and 2 and its associated principal plane.

## Slide 72: EXAMPLE 9.9 (SOLN)
Principal stresses
The element is orientated such that x’ axis or 2 is directed 22.5 counterclockwise from the horizontal x-axis.

## Slide 73: EXAMPLE 9.10
State of plane stress at a pt is shown on the element. Determine the maximum in-plane shear stresses and the orientation of the element upon which they act.

## Slide 74: EXAMPLE 9.10 (SOLN)
Construction of circle
Establish the ,  axes as shown below. Center of circle C located on the -axis, at the pt:

## Slide 75: EXAMPLE 9.10 (SOLN)
Construction of circle
Pt C and reference pt A (20, 60) are plotted. Apply Pythagoras theorem to shaded triangle to get circle’s radius CA,

## Slide 76: EXAMPLE 9.10 (SOLN)
Maximum in-plane shear stress
Maximum in-plane shear stress and average normal stress are identified by pt E or F on the circle. In particular, coordinates of pt E (35, 81.4) gives

## Slide 77: EXAMPLE 9.10 (SOLN)
Maximum in-plane shear stress
Counterclockwise angle s1 can be found from the circle, identified as 2s1.

## Slide 78: EXAMPLE 9.10 (SOLN)
Maximum in-plane shear stress
This counterclockwise angle defines the direction of the x’ axis. Since pt E has positive coordinates, then the average normal stress and maximum in-plane shear stress both act in the positive x’ and y’ directions as shown.

## Slide 79: EXAMPLE 9.11
State of plane stress at a pt is shown on the element. Represent this state of stress on an element oriented 30 counterclockwise from position shown.

## Slide 80: EXAMPLE 9.11 (SOLN)
Construction of circle
Establish the ,  axes as shown. Center of circle C located on the -axis, at the pt:

## Slide 81: EXAMPLE 9.11 (SOLN)
Construction of circle
Initial pt for  = 0 has coordinates A (8, 6) are plotted. Apply Pythagoras theorem to shaded triangle to get circle’s radius CA,

## Slide 82: EXAMPLE 9.11 (SOLN)
Stresses on 30 element
Since element is rotated 30 counterclockwise, we must construct a radial line CP, 2(30) = 60 counterclockwise, measured from CA ( = 0).
Coordinates of pt P (x’, x’y’) must be obtained. From geometry of circle,

## Slide 83: EXAMPLE 9.11 (SOLN)
Stresses on 30 element
The two stress components act on face BD of element shown, since the x’ axis for this face if oriented 30 counterclockwise from the x-axis.
Stress components acting on adjacent face DE of element, which is 60 clockwise from +x-axis, are represented by the coordinates of pt Q on the circle.
This pt lies on the radial line CQ, which is 180 from CP.

## Slide 84: EXAMPLE 9.11 (SOLN)
Stresses on 30 element
The coordinates of pt Q are
Note that here x’y’ acts in the y’ direction.

## Slide 85: 9.5 STRESS IN SHAFTS DUE TO AXIAL LOAD AND TORSION
Occasionally, circular shafts are subjected to combined effects of both an axial load and torsion.
Provided materials remain linear elastic, and subjected to small deformations, we use principle of superposition to obtain resultant stress in shaft due to both loadings.
Principal stress can be determined using either stress transformation equations or Mohr’s circle.

## Slide 86: EXAMPLE 9.12
Axial force of 900 N and torque of 2.50 Nm are applied to shaft. If shaft has a diameter of 40 mm, determine the principal stresses at a pt P on its surface.

## Slide 87: EXAMPLE 9.12 (SOLN)
Internal loadings
Consist of torque of 2.50 Nm and axial load of 900 N.
Stress components
Stresses produced at pt P are therefore

## Slide 88: EXAMPLE 9.12 (SOLN)
Principal stresses
Using Mohr’s circle, center of circle C at the pt is
Plotting C (358.1, 0) and reference pt A (0, 198.9), the radius found was R = 409.7 kPA. Principal stresses represented by pts B and D.

## Slide 89: EXAMPLE 9.12 (SOLN)
Principal stresses
Clockwise angle 2p2 can be determined from the circle. It is 2p2 = 29.1. The element is oriented such that the x’ axis or 2 is directed clockwise p1 = 14.5 with the x axis as shown.

## Slide 90
Question 5 Final Exam 2006
A rod in Figure 9 has a circular cross section with a diameter of 5 mm. It is subjected to a torque of 15 N. mm and a bending moment of 10 N. mm;
Determine the maximum normal stress and maximum shear stress. (4 marks) Determine the principal stresses at the point of maximum flexural stress. (3 marks) Sketch Mohr’s circle for this case with all the necessary points. (8 marks)
T = 15 N.mm
M = 10 N.mm