## Slide 1: Core Thermal Design
Mohsin Mohd Sies
Muhammad Syahir Sarkawi
Universiti Teknologi Malaysia
mohsin@utm.my
http://www.mohsin-sies.com

## Slide 4: Motivation
Thermal (not nuclear) considerations limit the amount of reactor power generation
Temperatures anywhere in the core must not exceed material property limitations (fuel, cladding)
Otherwise fuel element damage might result in release of large quantities of radioactive material into coolant, or in-core fuel meltdown.

## Slide 5
Motivation: Why Thermal Design Matters
Thermal (NOT nuclear) considerations limit reactor power generation
A 1,000 MW(electric) reactor generates ~3,300 MW(thermal) of heat
~30,000 fuel rods must be cooled simultaneously
Temperature rise from inlet to outlet: 20-35°C
Failure to remove heat → catastrophic temperature rise in seconds
Temperatures MUST NOT exceed material property limits (fuel, cladding)

## Slide 6
Introduction

## Slide 7
Introduction
Reactors must be designed in such a way that the fission products always remain confined within the fuel; throughout
  the operational lifetime of the core,
  during shutdown,
  under accident conditions,
  when the fuel may be denied normal cooling
The reactor power generation is limited by thermal rather than nuclear

## Slide 8
Introduction
The accepted design criterion
  the integrity of the cladding must be maintained through all operations,
  the expansion of the fuel on melting cannot rupture the cladding,
  the fuel must not melt
The melting point of which depends on burnup; that is on the fraction of the fissile atoms that have undergone fission
  generally, between 5,000 - 5,100 (2,760 - 2,815 )
  maximum fuel temperature below 4,500 (2,480 )

## Slide 9
General Considerations

## Slide 10
The rate at which heat is removed in a heterogeneous reactor core
First factor, , is governed (1) by the heat transfer by conduction through the fuel elements, cladding and other structures, if any separating these elements from the coolant and (2) the heat transfer be convection to the coolant
General Considerations
(1)
: Heat removal rate,
: Overall heat transfer coefficient=,
: Area across which heat is transferred,
: Mean temperature between heat generator and coolant,

## Slide 11
General Considerations
Coolant
Fuel pellet
Cladding
Small gap
Figure 1: Cross-sections of a conventional fuel pellet

## Slide 12
General Considerations
Fuel cladding should have high thermal conductivity
Other considerations should be taken into considerations such as low neutron absorption cross section, workability, withstand high temperatures and withstand corrosive action by coolant fluid.
Typical cladding materials, stainless steel, aluminum, zirconium and magnesium.
The resistance to heat conduction in the cladding is then reduced by holding the cladding thickness to a minimum.
The heat transfer by convection to the coolant is dependent on the coolant’s physical characteristics and on operating conditions, such as the coolant velocity
The second factor, , is the heat-transfer surface. The circumferential area of all the fuel elements, that must be designed within the reactor core
The third factor, , is the mean difference between the temperatures of the coolant and fuel.

## Slide 13
Barrier | Material | Limit | Function
1st | Fuel pellet (UO₂) | 2,800°C (melting) | Contains fission products
2nd | Cladding (Zircaloy) | 1,200°C (2,200°F) | Containment barrier
3rd | Reactor Coolant System | N/A | Confines radioactivity
Three Barriers Concept (Defense in Depth)

## Slide 14
Fuel Centerline Temperature: 1,200°C Design Limit
UO₂ ductility degrades above 1,600°C
Pellet densification & fission gas release accelerates above 1,200°C
At melting (2,800°C): fuel swells, pressurizes rod internally
Design margin: 40-50% to melting point
Safety factor: 2.3× on absolute melting point
Historical context: Three Mile Island (1979) → centerline temps exceeded 2,800°C

## Slide 15
Cladding Temperature & DNB Ratio Limits
Cladding Inner Surface Temperature (1,260°C):
Ductility loss → brittle fracture risk
Stress corrosion cracking susceptibility increases above 1,050°C
Creep strain limits: <1% to preserve cooling geometry
Departure from Nucleate Boiling (DNB) Ratio > 1.25 (PWR):
Nucleate boiling: h = 10,000-100,000 W/m²·K
Film boiling: h = 1,000-5,000 W/m²·K (10-100× drop)
Cladding temperature spikes 100-200°F in seconds after DNB
DNBR = 1.25 means actual heat flux = 80% of CHF (20% safety margin)

## Slide 16
Operational Lifetime: Normal Operation
Full Power (100%):
Typical: 18-24 months between refueling
Fuel burnup: 40-60 GWd/MTU (gigawatt-days per metric ton uranium)
Load Following (70-110% power):
Ramping rates: 3-5% power change per minute
Slower ramps provide better thermal margin
Low Power Operation (20-50%):
Testing, startups at reduced temperature
Different thermal challenges than full power

## Slide 17
Accident Conditions & Design Basis
Design Basis Accidents (DBA):
Loss of Coolant Accident (LOCA): Core partially uncovered
Loss of Flow: Pump trip with degraded heat removal
Reactivity Insertion: Control rod withdrawal
Core remains coolable; limited fuel damage allowed
Design Extension Conditions (DEC):
Beyond DBA but within engineering analysis capability
Core geometry remains maintainable, coolability preserved
Core Denied Normal Cooling:
Current reactors: ~2,000 seconds without cooling
Advanced designs (AP1000): >24 hours with passive cooling

## Slide 18
From Fission to Heat Flux
Neutron flux → volumetric heat generation → linear heat rate → surface heat flux → coolant boiling
Start at the core level
Average volumetric heat generation:
Idealized bare-core peaking (cylindrical):
Then go to the rod
Linear heat rate (per rod):
[W/m]
Surface heat flux (on cladding OD):
[W/m²]
Unit ladder
Pth [W]
q‴ [W/m³]
q′ [W/m]
q″ [W/m²]
Common mistake: mixing “per rod” vs “per assembly”.

## Slide 19
Gap Conductance Model
h_gap = (k_He / t_gap) + h_contact
where:
k_He = 0.2 W/m·K (helium thermal conductivity)
t_gap = 0.1 mm initially (gap thickness)
h_contact = mechanical contact dependent
Typical Values:
BOL: 1,500-2,500 W/m²·K (gas conduction + partial contact)
Mid-life: 3,000-8,000 W/m²·K (full contact + high pressure)
EOL: 2,000-5,000 W/m²·K (fission gas release reduces pressure)

## Slide 20
Heat Flux Definition: LHGR with Example
Linear Heat Generation Rate = Heat per unit length of rod
Example: 27.3 kW rod / 366 cm height = 27,300 W ÷ 366 = 74.6 W/cm
Typical PWR Values (3000 MWth plant):
Core average LHGR: 170 W/cm (at full power)
Radial peak (F_r = 1.20): 204 W/cm
With axial peak (F_z = 1.35): 275 W/cm theoretical max
Design limit: 220 W/cm (20% margin includes uncertainties)
Heat Flux Conversion: 220 W/cm → q'' ≈ 760 kW/m² (0.76 MW/m²)

## Slide 21
Heat Flux Definition: LHGR with Example
Linear Heat Generation Rate = Heat per unit length of rod
Typical PWR Values (3000 MWth plant):
Take a standard 17×17 Westinghouse‑type fuel assembly:
Fuel assemblies: 193 per core (typical 4‑loop PWR).​
Fuel rods per assembly: 264 (17×17 geometry).​
Total fuel rods in core: rods.​
Active (heated) fuel length: about 3.6 m = 360 cm.​
Core thermal power: .
Total heated length in the core:
Average LHGR (core‑average linear power):

## Slide 22
LHGR: Axial theoretical max Example
Once the core‑average LHGR is calculated, we use typical peaking factors:
Radial peaking factor: .
Axial peaking factor: .
Step 1 – hottest assembly (radial peak):
Step 2 – hottest axial location within that assembly:
So with these typical core numbers and peaking factors, you get:
Core‑average LHGR ≈ 170 W/cm.
Hottest‑spot “theoretical max” ≈ 275 W/cm when both radial and axial peaks line up.

## Slide 23
Temperature vs. Heat Flux (PWR Example)
For single-phase liquid cooling:
Fuel centerline relies on entire thermal path:
ΔT_fuel + ΔT_gap + ΔT_clad + ΔT_convection
Example: 220 W/cm rod at hottest elevation (q'' = 760 kW/m²):
Bulk coolant: 320°C (outlet region)
Convection ΔT (h = 50,000 W/m²·K): 760,000/50,000 = 15.2°C
Clad outer surface: 320 + 15.2 = 335.2°C
Clad inner (k=18, t=0.57mm): +~25°C = 360°C
Gap ΔT (h_gap=2000 W/m²·K): 760,000/2,000 = 380°C
Fuel pellet outer: 360 + 380 = 740°C
Fuel centerline (k=3.5 W/m·K): +460°C = 1,200°C ← Design limit!

## Slide 24
Problem 1 – Fuel centerline temperature
Fuel: UO₂ cylindrical pellet Radius
Thermal conductivity LHGR = 200 W/cm = 20,000 W/m
Gap conductance
Clad inner surface temperature
Volumetric heat generation (uniform):
Temperature drop fuel surface → clad inner (gap):
So fuel surface temperature:
Centerline–surface drop for a cylinder with uniform :
Centerline temperature:
Check vs 2,200°F ≈ 1204°C → safe, below limit.

## Slide 25
Fuel centerline temperature
The temperature difference between the centerline and the surface of a solid cylinder (fuel rod) with uniform volumetric heat generation and thermal conductivity , radius .​
Physical meaning
Heat is generated everywhere inside the fuel pellet, not just at the surface.
The center is farthest from the coolant, so it must conduct heat through the whole radius to reach the surface.
The result for a long cylinder with no axial variation and uniform is a parabolic temperature profile:
so at :

## Slide 26
Core Thermal Design Considerations

## Slide 27: Core Thermal Design
Core thermal design is an art of compromise
An iterative process (interdependence of heat flux and water density)
Overall plant characteristics is influenced by thermal hydraulic considerations

## Slide 28: Core Thermal Design
Once core basic lattice has been determined from nuclear, hydraulic, and heat transfer, the overall size of core becomes a sole function of thermal considerations
Parameters
  Fuel temperature distribution (most important)
  Specific power
  Power density
  Heat flux

## Slide 29: Core Design Objectives
Maximize core power density
Maximize attainable fuel burnup
Minimize cost of electricity
High outlet temperature for higher thermal efficiency
But temperatures of fuel and cladding anywhere in core must not exceed safe limits (material limitation)

## Slide 30: Design Constraints

## Slide 31: Design Constraints

## Slide 32: Thermal Reactor Design
3 aspects of design considerations
  Nuclear Design
  Thermal-hydraulics Design
  Mechanical/Material Design

## Slide 33: Nuclear Design

## Slide 34: Thermal-hydraulics Design

## Slide 35: Mechanical/Materials Design

## Slide 36: Impact on various design areas

## Slide 37: Impact on various design areas

## Slide 38
Limits and
Safety Aspects

## Slide 39: Thermal Design Safety Aspects
DNB Ratio
Hot channel, hot spot factors
Thermal limits
  Fuel centerline temperature
  Cladding inner surface temperature
Values change with fuel burnup!

## Slide 40: Thermal Design Nomenclature (Nominal, Average, Peak, Maximum)

## Slide 41: Thermal Design Nomenclature: From Core Average to Limiting Hot Spot
Key idea: Thermal design proceeds by successive peaking and uncertainty amplification, moving from a benign average to a conservative worst-case local condition.
Vertical progression (bottom → top):
Nominal core-average condition
  Total reactor power
  Core-average heat flux
  Core-average coolant temperature rise
Radial peaking applied
  Selects the hottest fuel assembly
  Accounts for radial neutron flux distribution
Axial + local peaking applied
  Selects hot axial elevation
  Selects hottest fuel pin / subchannel
Engineering & process uncertainties applied
  Manufacturing tolerances
  Flow maldistribution
  Instrumentation uncertainty

## Slide 42: Thermal Design Nomenclature: From Core Average to Limiting Hot Spot
Level 1: Core-average heat flux
This is never used directly for safety limits.
Level 2: Apply radial peaking factor
Where
Now we are at:
Axially averaged, radially hottest fuel assembly

## Slide 43: Thermal Design Nomenclature: From Core Average to Limiting Hot Spot
Level 3: Apply axial & local peaking
Typical meanings:
: axial flux shape (≈ sinusoidal)
: pin-to-pin / subchannel peaking
This corresponds to:
Nominal peak steady-state hot spot (no uncertainties yet)
Level 4: Apply engineering & process uncertainties
Where:
This is the maximum peak steady-state condition shown at the top of the figure.

## Slide 44
Example – Power Peaking
= 300 kW/m²
  = 1.5, = 1.4, = 1.1
  = 693 kW/m²
  Engineering uncertainty = 1.2
  ≈ 830 kW/m²

## Slide 45: Thermal Design Margin

## Slide 46: Thermal Design Limits

## Slide 47: Thermal Design Limits

## Slide 48: Thermal Design Limits
Parameter | Typical Limit | Why it matters
Fuel centerline T | < ~2200°C | Prevent fuel melting
Cladding T | < ~1200°C | Avoid oxidation & burst
DNBR / MDNBR | > 1.17–1.3 | Prevent DNB
Heat flux | Below CHF | Avoid burnout

## Slide 49
DNB Ratio

## Slide 50
Boiling Crisis for LWR

## Slide 51
Evaluation by Local Heat Flux (PWR)

## Slide 52: PWR: CHF and MDNBR Evaluation
CHF evaluated at hot spot conditions
  Design criterion: MDNBR > licensing limit (~1.3)
  If violated → reactor power must be reduced

## Slide 53: Example – PWR & MDNBR
Given max local heat flux = 830 kW/m²
  Local pressure = 15.5 MPa, mass flux = 4000 kg/m²·s
  CHF correlation gives = 1400 kW/m²
  Minimum DNBR =
  MDNBR = 1400 / 830 ≈ 1.69 (> 1.3 → SAFE)

## Slide 54: Example – DNBR with W‑3 style data
Given local conditions at the hot spot: Local heat flux
Critical heat flux from W‑3 correlation at this location:
So:
This is > design limit 1.25 → adequate margin.​
Now assume system pressure drops 5% and CHF reduces by 10% :
New CHF: .
Heat flux unchanged:
Still > 1.25 but margin is smaller; additional transients could push it closer to the limit.

## Slide 55: BWR: Dryout and Critical Power Ratio (CPR)
Dryout occurs when liquid film on cladding vanishes
  Critical power determined at hot spot
  MCPR must exceed safety limit

## Slide 56: Example – BWR Dryout / CPR
Actual assembly power = 3.0 MW
  Critical power from correlation = 4.2 MW
  CPR = 4.2 / 3.0 = 1.40
  MCPR > 1.25 → SAFE from dryout

## Slide 64: Thermal Crisis Summary
MDNBR > 1.17 (Japan)

## Slide 65
Hot Channel & Hot Spot Factor
Hot spot factor (hot-channel factor) is safety factor or margin multiplied to the calculated nominal fluxes.
In any reactor, the extent to which exceeds the average heat flux in the core is given by the hot channel factor, also called the hot spot factor, F.
(4)
: is the average heat flux in the core

## Slide 66: Hot-spot Factors
Deviation from nominal values are contributed by
  Nuclear hot-spot factors
  Engineering hot-spot factors

## Slide 67: Nuclear Hot-spot Factors
Deviations due to
  Partially inserted control rods
  Nonhomogeneities
    Moderator (boiling)
    Fuel
    Structural and other materials

## Slide 68: Engineering Hot-spot Factors
Deviations due to
  Mechanical subfactors
    Manufacturing tolerances (clad thickness)
    Warping of fuel elements
  Flow distribution subfactors
    Maldistribution of coolant flow
    Heat transfer coefficient, h
    Fuel element dimensions

## Slide 69
Manufacturing tolerances in the fuel assemblies ,may result in slight bowing of the fuel rods, leading to reduced coolant flow and excessive heating of a portion of the fuel.
Hot Channel & Hot Spot Factor
(Engineering Hot Spot Factor)

## Slide 70
Fluctuations in the thickness of the cladding may give rise to hot spots where the cladding is thinnest. (thin cladding leads to a larger gap, hence a larger between fuel pellet and cladding)
Also, certain aspects of the coolant flow are inherently statistical in character and tend to give fluctuations in the heat flux.
These various mechanisms by which differ from its computed value, describe by the engineering hot channel factor
Hot Channel & Hot Spot Factor
(Engineering Hot Spot Factor)

## Slide 71: Hot-spot Factors (classified by effects)
By effects on temperature or enthalpy of fuel and coolant
  Factor for temp. rise of coolant from core inlet conditions,
  Factor for temp. rise across coolant boundary layer,
  Factor for temp. rise across fuel element,

## Slide 73: Overall Hot-spot Factor
Combining hot-spot subfactors, f, to get overall hot-spot factor, F.
Methods;
  Multiplicative
    All deviation factors are assumed to take place simultaneously at the same point.
    Overly conservative result
  Statistical
    Many deviation factors are independent of each other
    Small probability of occurring at the same point
    More realistic result

## Slide 74
Hot Channel & Hot Spot Factor
(Overall Hot Spot Factor)
The overall hot channel is then
Each of the individual mechanisms is described, in turn, by an engineering hot channel factor,
The engineering subfactors are obtained from data on fabricated reactor components or from tests.
For instance, the amount of fissile material per unit length of the fuel rods. For a given thermal flux, is very nearly proportional to . When measurements of are carried out on manufactured rods, it is found that the actual values form a normal distribution about some mean or average value shown in Figure 3
(6)

## Slide 75
All values of are presumably possible. However, specific values of become less and less likely with increasing deviation from the mean.
Figure 3: Normal distribution of measured values of

## Slide 76
Hot Channel & Hot Spot Factor
It shown that probability that exceeds by more than , where is standard deviation pf the distribution (1.35 per 1,000 an unlikely occurrence)
In those situations like the one just described, in which is proportional to a normally distributed engineering variable , the engineering subfactor is defined as
(7)
: is the value of
: is the standard deviation

## Slide 77
Hot Channel & Hot Spot Factor Example

## Slide 78
Problem 3 – Hot‑spot factor, multiplicative vs statistical
Nominal local heat flux:
Independent hot‑spot subfactors (1σ‑type):
nuclear radial = 1.10
nuclear axial = 1.15
manufacturing = 1.05
flow maldistribution = 1.06
CHF correlation bias = 1.04​
(a) Multiplicative (deterministic, conservative)
Peak heat flux:

## Slide 79
(b) Statistical – root sum of squares (RSS for random parts)
Treat as systematic (always applied), and as random.
Systematic factor:
Random deviations: :
, ,
RSS combination:
Effective random factor:
Overall statistical hot‑spot factor:
Peak heat flux (statistical):
So statistical method gives lower but still conservative hot‑spot than pure multiplication.

## Slide 80
Example - Hot Channel & Hot Spot Factor
The thermal design calculation gives a calculated nominal hot-channel linear heat rate
We will compute an engineering hot-channel factor to find
(And in full form with nuclear peaking:
Given 3 independent uncertainty contributors (typical independent contributors to “hotness”)
Fuel loading (manufacturing): mean , standard deviation
Flow maldistribution: fractional standard deviation (i.e. 2%)
Heat transfer coefficient : fractional standard deviation (i.e. 1%)

## Slide 81
Example - Hot Channel & Hot Spot Factor
Individual “3σ” subfactors (per Lamarsh)
Lamarsh defines an engineering subfactor for a variable as
So for contributor (1),
For (2) and (3), since they’re already fractional:

## Slide 82
Example - Hot Channel & Hot Spot Factor
Multiplicative method (for comparison)
Then
Statistical method (simple “RSS of σ” approach)
If the contributors are independent and deviations are small, combine fractional standard deviations by root-sum-square (RSS):
Then take a one-sided 3σ bound for the combined effect:
So

## Slide 83
Core Design Walkthrough

## Slide 84
Reactor Design
The final reactor design necessarily represents a series of compromises between nuclear and thermal-hydraulic factors which all made in the interest of safety and economy.
In designing a reactor, there is overlap between those problem that are specifically nuclear
  The neutron flux
  Power distributions
  Transient behavior
Thermal Hydraulics
  Those factors involving the removal of heat from the system

## Slide 85
Reactor Design
Once core basic lattice has been determined from nuclear, hydraulic, and heat transfer, the overall size of core becomes a sole function of thermal considerations
Parameters
  Fuel temperature distribution (most important)
  Specific power
  Power density
  Heat flux

## Slide 86
Reactor Design
Consider the design of a specified type of power reactor having a given thermal power output.
The first problem is the selection of the core materials
  Chosen on previous experience, availability and cost
  The amount and enrichment of the fuel including estimates of core lifetime and radiation damage to the fuel elements.
Second, a fuel lattice arrangement is then computed for the proposed fuel.
  The operating parameters of the reactor-the neutron flux,
  The power and temperature distributions,
  The coolant density and/or void distribution
  The temperature and heat flux along the hot channel

## Slide 87
Reactor Design
Such computations are inherently iterative, at least for some types of reactors.
With the PWR and BWR, it is necessary to know the water density as a function of position to compute the neutron flux and the power distribution.
However, the power distribution must be known before the water density.
We must assume some density distribution to start with, say, unity throughout the core.
The flux and power distributions are computed with this water density and a new density distribution is determined from the computed heat flux.

## Slide 88
Reactor Design
The neutron flux and power distributions are now computed using this new density distribution, and this in turn leads to a third density distribution.
The calculations are obtained until the density distribution provides a power distribution that gives the same density distribution.

## Slide 89
Reactor Design
During early stage in the design of the core, the neutron flux is usually obtained from a multigroup diffusion calculation using only a few groups.
To reduce computation costs, multigroup calculations with many groups are normally performed in the final stages of the design.
If the reactor is water cooled, the DNB ratio is next computed as a function of distance along the hottest channel.
The minimum DNBR must equal to some preset limiting value.

## Slide 90
Reactor Design
If the computed DNBR is not equal to this value then the parameters of the lattice or the coolant flow are changed, the previous calculations of the core are repeated and a new DNBR is obtained.
These computations are repeated until minimum value of DNBR is found.
Also determines the maximum heat flux, does not necessarily occur at the point where the DNBR is smallest.

## Slide 91
Reactor Design
If the reactor is not water cooled, is determined solely by the limiting value of the fuel temperature,
The overall hot channel factor, F, is obtained using the methods discussed earlier. The average heat flux throughout the core can then be computed from
This provides the reactor with the desired margin of safety.
(8)

## Slide 92
Reactor Design
Once is known, the total heat transfer area can be found from
Finally, from the heat transfer and the dimensions of the fuel rods, it is possible to compute the total number of rods required in the reactor.
(8)
(9)
(10)
& : are the fuel material diameter and density
: total length
: total mass

## Slide 93
Reactor Design
This number will undoubtedly be different from the one used at the start of the design.
Many of the foregoing calculations must be repeated until a completely self-consistent reactor is obtained.
At this point, detailed multigroup and two-dimensional neutron diffusion calculations can be undertaken, along with various transient analyses and lifetime-burnup computations, to refine the design.

## Slide 94
Reactor Design Exercise
A PWR has a core consists of fuel rods 10 ft long and 0.6 in. in diameter. The reactor operates at a thermal power of 3,000 MW; it has a maximum calculated heat flux of 539,000 Btu/hr- and an overall hot channel factor of 2.80. Calculate the total heat transfer area and the number of fuel rods in the core.
The average heat flux is given by:

## Slide 95
With the reactor power of 3,000 MWt = the heat transfer area is
Reactor Design Exercise
The surface area of each fuel rod is 10
The total number of rods is then

## Slide 96
Plant and Core Thermal Design Procedure

## Slide 97
Core Thermal Design
The detailed design of a core, however is a compromise between
  nuclear,
  material,
  structural,
  hydraulic,
  heat-transfer,
  economic
considerations, usually involving on iterative procedure to arrive at an optimum.

## Slide 98
Core Thermal Design
The most important parameter in the thermal design (hydraulic and heat transfer) is the fuel temperature distribution.
The specific power (kW(t)/kg), power density (kW(t)/liter) and heat flux (Btu/hr ) for once a basic fuel lattice have chosen.
They must be limited so that, together with the designed heat removal system (h) they would not result in temperatures that exceed fuel element material limitations and therefore in fuel element failure.

## Slide 99
In thermally designing a core one begins with several basic requirements, obtained from the power plant and steam cycle as the following:
The net power output in MW(e) is determined by the electric utility ordering the plant, based on demand.
The type of reactor is selected by the electric utility based on competitive or sometimes on a desire to gain experience in a new field or type of power plant or reactor.
The system cycle is designed, including the number of feedwater heaters, reheat stages, etc,. and the main and auxiliary power components selected and the main steam conditions established.
Plant and Core Thermal Design
Procedure

## Slide 100
Based on previous parameters, the net thermal efficiency of the power plant is determined.
The reactor output in MW(t) is now computed.
A basic fuel lattice (cell or subassembly) is determined from nuclear, hydraulic and heat-transfer considerations.
  These include fuel type and enrichment, cladding, fuel elment diameter, moderator to fuel ratio, etc.
  Often the choice of fuel type and fuel element diameter are predicted on the existence of manufacturing facilities for a particular type and size.
Reactor and Core Thermal Design
Procedure

## Slide 101
For a liquid-cooled core (PWR, BWR, etc.), a critical (burnout) heat flux is obtained from appropriate data or correlation. This may be reduced by a safety margin
An overall hot-spot factor is determined.
The core average heat flux, may now be determined
(11)
Reactor and Core Thermal Design
Procedure

## Slide 102
From , the total heat transfer surface (cladding surface) are , is determined
From the known fuel element cladding diameter the total length, , and total mass, , of the fuel are determined
(11)
: is the total thermal energy output of the core, obtained in step 5
(9)
(10)
& : are the fuel material diameter and density
: total length
: total mass
Reactor and Core Thermal Design
Procedure

## Slide 103
The overall core shape is now determined, e.g., an upright cylinder of a certain height to diameter ratio, commensurate with pressure drops, reactor pressure vessel diameter, etc.
The maximum fuel cladding and centre line temperatures are now checked using the individual hot-spot factors to ascertain that they do not exceed material limitations
Further reading on max temperature:
https://www.nuclear-power.net/nuclear-engineering/heat-transfer/heat-generation/temperature-profile-nuclear-fuel/
https://allthingsnuclear.org/dlochbaum/nuclear-safety-temperature-calculations-wheres-jethro/
Reactor and Core Thermal Design
Procedure

## Slide 104
The number and type of the control rods, are designed into the system and checked against nuclear, control and excess reactivity requirements for the new and equilibrium cores, e.g., a certain excess reactivity should be built into the core to overcome fuel depletion effects and still maintain good control rod position in the core.
The reactor vessel, core support structure, thermal shields, biological shields, etc. are now designed
Reactor and Core Thermal Design
Procedure

## Slide 105
Target core thermal power: PWR.
Assume:
50,000 rods, each active length 3.6 m → total heated length .
Coolant mass flow chosen such that average outlet enthalpy rise corresponds to 30°C at density 700 kg/m³.
Example – Simple design iteration

## Slide 106
Iteration 1 – initial guess
Assume uniform coolant density 700 kg/m³.
Neutronics gives flat power distribution → average LHGR:
Thermal calc with this LHGR predicts outlet temperature 325°C and density actually 650 kg/m³ (due to heating and some void).
Density is lower than assumed, which softens moderation → real power should shift slightly toward bottom of core.
Example – Simple design iteration

## Slide 107
Iteration 2 – update density and power
Use new density profile (650 kg/m³ near top, 700 near bottom) in neutronics.
Power shifts: mid‑core region now 10% higher than average; bottom 5% lower.
Recompute LHGR peak at mid‑core: .
Thermal calc with this shape shows DNBR minimum 1.30 and outlet 328°C; updated density profile is now 645–700 kg/m³
Example – Simple design iteration

## Slide 108
Iteration 3 – convergence
Repeat; changes in density and power shape between iteration 2 and 3 are <0.5%.
DNBR ≥ 1.25 everywhere, centerline T < 1200°C, so limits satisfied.
Result: self‑consistent design after a few iterations
Example – Simple design iteration

## Slide 109
Two options: PWR, 1000 MWe net, 33% efficiency → 3000 MWth core.
Option A – Conservative
Enrichment: 4.0 wt% U‑235
Core height: 3.9 m, diameter: 3.7 m → volume ≈ 44 m³
Power density:
Average LHGR: 160 W/cm
Minimum DNBR at full power: 1.80
Peak fuel centerline at EOL: 1050°C
Cycle length: 16 months
Fuel cost index (relative): 1.0
Capital cost index: 1.05 (larger vessel, more fuel assemblies)
Example – Trade‑off analysis (conservative vs aggressive core)

## Slide 110
Option B – Aggressive
Enrichment: 5.0 wt% U‑235
Core height: 3.6 m, diameter: 3.3 m → volume ≈ 31 m³
Power density:
Average LHGR: 190 W/cm
Minimum DNBR at full power: 1.35
Peak fuel centerline at EOL: 1150°C (closer to 1200°C limit)
Cycle length: 22 months (more burnup per batch)
Fuel cost index: 0.9 (fewer assemblies, but higher enrichment)
Capital cost index: 0.95 (smaller vessel, less structural material)
Example – Trade‑off analysis (conservative vs aggressive core)
Comparison:
Option A: lower power density and more generous thermal margins (DNBR, ), but higher capital cost and shorter cycles.
Option B: more compact and economical per MW, but tighter safety margins and more demanding analysis/licensing.

## Slide 111: References
Todreas, Kazimi, Nuclear Systems, Thermal Hydraulic Fundamentals, CRC Press
Lamarsh, Introduction to Nuclear Engineering, Prentice-Hall
M M ElWakil, Nuclear Heat Transport, International Textbook Company
Buongiorno, Notes on Two Phase Flow, Boiling Heat Transfer, and Boiling Crises in PWRs and BWRs, MIT
Buongiorno, Boiling Crisis in LWRs, MIT
Reactor Thermal Engineering IIb, ITP @ JAEA, August 2010

## Slide 112: Classification of Plant States