## Slide 1: Thermodynamics I Chapter 2 Properties of Pure Substances
Mohsin Mohd Sies
Fakulti Kejuruteraan Mekanikal, Universiti Teknologi Malaysia

## Slide 2: Properties of Pure Substances (Motivation)
To quantify the changes in the system, we have to be able to describe the substances which make up the system.
The substance is characterized by its properties.
This chapter shows how this is done for two major behavioral classes of substance covered in this course; phase-change fluids, and gases.

## Slide 3
PURE SUBSTANCE
3 major phases of pure substances;
Solid
Liquid
Gas
  plasma

## Slide 4
Phase Change of Pure Substances ex. Water at 1 atm of pressure
T=25oC
T=100oC
T=100oC
Saturated vapor
Saturated liquid
Not about to evaporate
Heat added T
Compressed liquid phase
About to evaporate
Heat added evaporation starts
Saturated liquid phase
Heat added continues evap.
T unchanged
Wet steam or
Saturated liquid-vapor mixture

## Slide 5
Phase Change of Pure Substances (ctd.) ex. Water at 1 atm of pressure
T=100oC
T=110oC
All liquid evaporated
(about to condense)
Heat removed condensation
Saturated vapor phase
Not about to condense
Heat added T
Superheated vapor phase

## Slide 7
Evaporation temperature changes with pressure
During phase change, temperature and pressure are not independent Tsat <-> Psat
Energy needed to vaporize (latent heat of vaporization) decreases with increasing pressure

## Slide 15
QUALITY, x (2 phase condition)
Saturated liquid-vapor mixture condition
x is a thermodynamic property
x exists only in the liquid-vapor mixture region
mvapor
mliquid
Degree of evaporation
Dryness fraction
quality
mvapor
mtotal
x

=


0  x  1
(wet)
100% liquid
(dry)
100% vapor

## Slide 16
Enthalpy of vaporization, hfg (Latent heat of vaporization): The amount of energy needed to vaporize a unit mass of saturated liquid at a given temperature or pressure.

## Slide 17
Quality (cont.)

## Slide 18
Some Additional Thermodynamic Properties
Internal Energy, U [kJ] Specific Internal Energy, u [kJ/kg]
Enthalpy, H [kJ] H ≡ U + PV Specific Enthalpy, h [kJ/kg] h = u + Pv
Entropy, S [kJ/K] Specific Entropy, s [kJ/kg.K]

## Slide 19
PROPERTY TABLES
3 types of tables
Compressed liquid table
Saturated table
Superheated table
Saturated tables
Temperature table – T in easy to read numbers
Pressure table – P in easy to read numbers

## Slide 20: Compressed Liquid Approximation
Because liquid is more sensitive to changes of temperature than that of pressure

## Slide 21
Choosing which table to use
Determine state (phase) first!
How? Compare the given properties against the saturated table
(ex. given h & T)
If hf ≤ h ≤ hg at the given T
→Mixture phase
→ use saturated table
If h > hg at the given T
→ Superheated phase
→ use superheated table
If h < hf at the given T
→ Compressed liquid phase
→ use saturated table

## Slide 22
Choice of tables (cont.)
If P & T is given
P ↔ Tsat
T ↔ Psat
P > Psat at the given T
T < Tsat at the given P
P < Psat at the given T
T > Tsat at the given P
Compressed liquid
Superheated vapor
Best determined by simple sketching of
the p-v or T-v diagram

## Slide 23
Choice of tables (additional)
(ex. given h & P)
If hf ≤ h ≤ hg at the given P
→Mixture phase
→ use saturated table
If h > hg at the given P
→ Superheated vapor phase
→ use superheated vapor table
If h < hf at the given P
→ Compressed liquid phase
→ use saturated table
P ↔ Tsat

## Slide 24
Notes on Using Property Tables
Some tables do not list h (or u) → u (or h) can be obtained from h = u + Pv
Values for compressed liquid is taken as the same as that of saturated liquid at the same temperature ex. T=25oC, P=1 bar (compressed liquid) h25C,1b hf@T=25C

## Slide 25
Interpolation (Linear Interpolation)
T
Ta
Tb
va
v=?
vb
Assume a & b connected by a straight line
a
b
Employ concept of slope

## Slide 26: Ideal Gas (Initial Observations)

## Slide 27
IDEAL GAS
(for pressures much lower than critical pressure)
Equation of state for ideal gas
R = Gas Constant [kJ/kg.K]
(constant for a gas, value depends on type of gas)
Can be used to relate between different states

## Slide 28
Ideal gas u, h, cp, cv relationship
Constant Volume Specific Heat Capacity cv
Constant Pressure Specific Heat Capacity, cp

## Slide 29
POLYTROPIC PROCESS
-Processes that obey/follow the path
pvn = c
n = polytropic index
p
v
pvn = c
p1v1n = p2v2n
1
2
Can be used to relate between two states

## Slide 30
n = 1 isothermal
n = 0 isobaric
n = const. volume
Some special cases for polytropic processes
Ideal Gas & Polytropic Process combined
Can be used to relate between two states

## Slide 31: Real Gases & Compressibility Factor

## Slide 33
Compressibility Factor
Reduced pressure
Reduced temperature
Pseudo-reduced specific volume

## Slide 35
H2O (Water, Steam)
Property Tables !!!
Ideal Gas
pV = mRT
& other relations
h = cpT
u = cvT
etc.
Air,
N2 , He, etc.

## Slide 36
Other Equations of State
Van der Waal’s :
Beattie-Bridgeman :
Benedict-Webb-Rubin :
Virial equations of state:

## Slide 37
The apparent and the implied
Some examples…
Constant volume (V=c)
Constant pressure (p=c)
Rigid tank
Frictionless cylinder, freely moving piston
The Implied
The Apparent