## Slide 1
Examples
A single-acting reciprocating compressor induces 1 m3 of air per minute at 1.013 b, 15 oC, and delivers it at 7 b. Compression follows pv1.35=c and the clearance can be neglected. Determine the indicated power.
If the compressor above operates at the speed N=300 rpm, determine the cylinder bore if the stroke to bore ratio is 1.5:1
Find the isothermal efficiency for the compressor above.

## Slide 2
Examples
A double-acting compressor induces 14 m3 air per minute at 1.013 b and 15 oC. Delivery pressure is 7 b and the compressor speed is 300 rpm. If the clearance volume is 5% of swept volume and compression index is 1.3, find Vs and indicated power.
Air at free air condition of 1.013 b and 15 oC enters a double-acting compressor at 14 m3/min. During the intake stroke, cylinder pressure is 0.95 b and the temperature is 32 oC. Delivery pressure is 7 b and the compression and expansion index is 1.3. If the clearance volume is 5% of the swept volume, find the volumetric efficiency.

## Slide 3
Examples
In a single-acting, 2 stage compressor, 4.5 kg/min of air is compressed from 1.013 b and 15 oC over a 9:1 pressure ratio. Both stages have the same pressure ratios and follow pv1.3=c for all compression and expansion processes. Clearance volume is 5% of the swept volume for both stages, and the compressor operates at 300 rpm. If intercooling is complete, find the indicated power and the swept volume for both stages.