## Slide 1: Thermodynamics II Chapter 4 Internal Combustion Engines
Mohsin Mohd Sies
Fakulti Kejuruteraan Mekanikal,
Universiti Teknologi Malaysia

## Slide 2: Coverage
Introduction
Operation of IC Engines
Ideal Cycles
  Otto Cycle
  Diesel Cycle
  Dual Cycle
Parameters
  Power
  Mean Effective Pressure
  Compression Ratio
  Cut-off Ratio
  Thermal Efficiency
Reciprocating Engine Performance
  Dynamometer
  Rates
  Mean Piston Speed
  Power
  Mean Effective Pressure
  Thermal Efficiency
  Volumetric Efficiency
  Mechanical Efficiency
  Specific Fuel Consumption

## Slide 3: Internal Combustion Engines
The internal combustion engine is an engine in which the combustion of fuel-oxidizer mixture occurs in a confined space for the purpose of converting the combustion heat into mechanical work
Applied in:
automotive
rail transportation
power generation
ships
aviation
garden appliances

## Slide 4: IC Engine Operation
IC Engines operate as
  4 stroke
  2 stroke
  Petrol
  Diesel

## Slide 5
4 Stroke Cycle Processes

## Slide 6
4 Stroke Cycle Processes

## Slide 7: Internal Combustion Engines – four stroke (Otto)
starting position
a. piston starts moving down
b. intake valve opens
c. air-fuel mixture gets in
1. intake
a. piston moves up
b. both valves closed
c. air-fuel mixture gets compressed
2. compression

## Slide 8: Internal Combustion Engines – four stroke -
ignition
a. air-fuel mixture explodes driving the piston down
3. power
a. piston moves up
b. exhaust valve opens c. exhaust leaves the cylinder
4. exhaust

## Slide 9: Internal Combustion Engines – 4 Stroke (Diesel)
air intake
compression
fuel injection
combustion
exhaust
exhaust /intake

## Slide 10
1. Induction 2. Compression 3. Power 4. Exhaust
Four-stroke cycle (or Otto cycle)

## Slide 11: Internal Combustion Engines – two stroke
1. Power / Exhaust
2. Intake / Compression
ignition
piston moves downward compressing fuel-air mixture in the crankcase
exhaust port opens
inlet port opens
compressed fuel-air mixture rushes into the cylinder
piston upward movement provides further compression

## Slide 13
Power / Exhaust (& Transfer)
Intake / Compression
2 Stroke Cycle Processes

## Slide 14
2 Stroke Cycle

## Slide 15: Configuration
Inline - The cylinders are arranged in a line, in a single bank
V - The cylinders are arranged in two banks, set at an angle to one another.
Flat - The cylinders are arranged in two banks on opposite sides of the engine
Radial

## Slide 16: Internal Combustion Engines – Radial

## Slide 17: Internal Combustion Engines – multi-cylinder -
V
flat
“boxer”
inline

## Slide 18: Internal Combustion Engines – multi-cylinder -
14 cylinder Diesel engine (80 MW)

## Slide 19: 4 Stroke vs 2 Stroke
Each process in own stroke
1 cycle = 2 crank revolution
1 power stroke per 2 crank rev.
More economical fuel consumption
Less pollution
More complicated mechanically
Processes share strokes
1 cycle = 1 crank revolution
1 power stroke per crank rev.
Less economical (fuel short circuiting)
More pollution
Simpler & lighter construction

## Slide 20: Petrol vs Diesel
Petrol as fuel
Otto Cycle
Spark Ignition (SI) (spark plug)
Compression ratio ~7:1 to ~11:1
Fuel-Air Mixture induced (carburetor)
Less economical fuel consumption
Diesel as fuel
Diesel Cycle
Compression Ignition (CI) (no spark plug)
Compression ratio ~12:1 to ~24:1
Only air is induced (fuel injection)
More economical fuel consumption

## Slide 21: Petrol vs Diesel (cont.)
Less pollution
Lighter & cheaper
More pollution
Heavier & more expensive
Both can be implemented using either 4 stroke or 2 stroke

## Slide 22: Classification
Conventional Reciprocating Internal Combustion Engine
By Mechanical Operation
4 Stroke
2 Stroke
Petrol (Otto)
(SI)
Diesel (CI)
By Thermodynamic Cycle
Otto
Diesel
4 Stroke
2 Stroke

## Slide 23
Piston-cylinder terminologies
TDC – Top Dead Center
BDC – Bottom Dead Center

## Slide 24
b – Bore, Diameter
s – Stroke
l – Connecting Rod Length
a – Crank Throw = ½ stroke
Piston-cylinder terminologies

## Slide 25
Review
SSSF Energy Equation
Relationship of P, v, T between two states under polytropic process for ideal gases
For an isentropic process
Specific Heat Ratio

## Slide 26
AIR-STANDARD ASSUMPTIONS
The combustion process is replaced by a heat-addition process in ideal cycles.
Air-standard assumptions:
The working fluid is air, which continuously circulates in a closed loop and always behaves as an ideal gas.
All the processes that make up the cycle are internally reversible.
The combustion process is replaced by a heat-addition process from an external source.
The exhaust process is replaced by a heat-rejection process that restores the working fluid to its initial state.
Cold-air-standard assumptions: When the working fluid is considered to be air with constant specific heats at room temperature (25°C).
Air-standard cycle: A cycle for which the air-standard assumptions are applicable.

## Slide 27
AN OVERVIEW OF RECIPROCATING ENGINES
Nomenclature for reciprocating engines.
Spark-ignition (SI) engines
Compression-ignition (CI) engines
Compression ratio
Mean effective pressure

## Slide 28: P-v diagram of real engines

## Slide 29
OTTO CYCLE: THE IDEAL CYCLE FOR SPARK-IGNITION ENGINES
Actual and ideal cycles in spark-ignition engines and their P-v diagrams.

## Slide 30
Schematic of a two-stroke reciprocating engine.
The two-stroke engines are generally less efficient than their four-stroke counterparts but they are relatively simple and inexpensive, and they have high power-to-weight and power-to-volume ratios.
T-s diagram of the ideal Otto cycle.
Four-stroke cycle
1 cycle = 4 stroke = 2 revolution
Two-stroke cycle
1 cycle = 2 stroke = 1 revolution

## Slide 31
The thermal efficiency of the Otto cycle increases with the specific heat ratio k of the working fluid.
Thermal efficiency of the ideal Otto cycle as a function of compression ratio (k = 1.4).
In SI engines, the compression ratio is limited by autoignition or engine knock.

## Slide 32
DIESEL CYCLE: THE IDEAL CYCLE
FOR COMPRESSION-IGNITION ENGINES
In diesel engines, the spark plug is replaced by a fuel injector, and only air is compressed during the compression process.
In diesel engines, only air is compressed during the compression stroke, eliminating the possibility of autoignition (engine knock). Therefore, diesel engines can be designed to operate at much higher compression ratios than SI engines, typically between 12 and 24.
1-2 isentropic compression
2-3 constant-volume heat addition
3-4 isentropic expansion
4-1 constant-volume heat rejection.

## Slide 33
Thermal efficiency of the ideal Diesel cycle as a function of compression and cutoff ratios (k=1.4).
Cutoff ratio
for the same compression ratio

## Slide 34
QUESTIONS ???
Diesel engines operate at higher air-fuel ratios than gasoline engines. Why?
Despite higher power to weight ratios, two-stroke engines are not used in automobiles. Why?
The stationary diesel engines are among the most efficient power producing devices (about 50%). Why?
What is a turbocharger? Why are they mostly used in diesel engines compared to gasoline engines.
P-v diagram of an ideal dual cycle.
Dual cycle: A more realistic ideal cycle model for modern, high-speed compression ignition engine.

## Slide 35: Performance Parameters
Can be measured by two ways
  Indicator equipment
  Dynamometer
Some parameters obtained
  Mean Piston Speed
  Mean Effective Pressure
  Power
  Mechanical Efficiency
  Thermal Efficiency
  Specific Fuel Consumption
  Volumetric Efficiency

## Slide 36: Indicator
Consists of
  Pressure Indicator (Pressure transducer)
  Crank angle encoder (crank angle gives cylinder volume)
  Tachometer (engine speed)
Purpose – to obtain pressure inside cylinder
Produces P-v diagram (Indicator diagram) of in-cylinder gas.
All parameters obtained from indicator diagram has prefix ‘indicated’. (indicated mean effective pressure, indicated power, etc.)

## Slide 37: Indicator

## Slide 38: Dynamometer
A dynamometer is coupled to the engine crankshaft
Measures torque at crankshaft
Torque measured by braking the engine and balancing the resulting torque with a load arm
Along with engine speed from tachometer, we can calculate engine power
All parameters obtained from dyno measurement are prefixed by ‘brake’.
Difference of in-cylinder (indicated) and crankshaft (brake) is the loss due to friction.

## Slide 39: Dynamometer

## Slide 40: Rates
To convert between a quantity and its rates, multiply with N’ (number of power strokes per second)
N = speed
Thus, for power – work, mass flow rate – mass, etc.

## Slide 41: Mean Piston Speed
Useful to compare between different engines

## Slide 42: Indicated Mean Effective Pressure
Indicated Mean Effective Pressure (IMEP = Pi)
The constant depends on the scale of the recorder. For mechanical indicator, it is the spring constant.

## Slide 43: Indicated Mean Effective Pressure

## Slide 44: Indicated Work, Indicated Power

## Slide 45: Brake Power
From the dynamometer reading of torque where W = dyno load, R = dyno arm length,
Brake Power (shaft power) is given by

## Slide 46: Friction Power, Mechanical Efficiency
Friction power is the power lost during transmission from in-cylinder (indicated power) to the crankshaft (brake power) FP = IP – BP
So, we can define the mechanical efficiency of the engine
Normal values around 80 – 90%

## Slide 47: Brake Mean Effective Pressure (BMEP)
From mechanical efficiency, we can write
Combining with expression of IP (indicated power)
To make expression of BP look similar to IP
Where Pb is called the brake mean effective pressure (BMEP)
Can also be related as
BMEP is independent of engine size

## Slide 48: Thermal Efficiency
Thermal efficiency is basically
If we use indicated power for net power, we get indicated thermal efficiency
If brake power is used, we get brake thermal efficiency
We can also relate mechanical efficiency

## Slide 49: Specific Fuel Consumption (SFC)
A measure of engine economy
Can be used to compare performance of engines of different sizes.
Noticing the ratio in brake thermal efficiency, we can also write brake thermal efficiency as
[kg/kW.hr]

## Slide 50: Volumetric Efficiency
Breathing capacity of the engine
The free air condition is the atmospheric condition, P0, T0. So, md is
Can also be defined in terms of volumes with
In terms of rates,