## Slide 1: Chapter 8 : Natural Convection
Contents:
Physical consideration, governing equation
Analysis of vertical, horizontal & inclined plates
Analysis of cylinder, sphere & enclosures

## Slide 2: Chapter 8 : Natural Convection
What is buoyancy force ?
The upward force exerted by a fluid on a body completely or partially immersed in it in a gravitational field.
The magnitude of the buoyancy force is equal to the weight of the fluid displaced by the body.

## Slide 3: Chapter 8 : Natural Convection

## Slide 4
The coefficient of volume expansion is a measure of the change in volume of a substance with temperature at constant pressure.
Thermal expansion coefficient / Volume expansion coefficient: Variation of the density of a fluid with temperature at constant pressure.
Ideal gas
The larger the temperature difference between the fluid adjacent to a hot (or cold) surface and the fluid away from it, the larger the buoyancy force and the stronger the natural convection currents, and thus the higher the heat transfer rate.

## Slide 5: Chapter 8 : Natural Convection
- Ratio of buoyancy forces and thermal and momentum diffusivities.

## Slide 6: Rayleigh Number, Ra=Gr.Pr
In fluid mechanics, the Rayleigh number for a fluid is a dimensionless number associated with buoyancy driven flow (also known as free convection or natural convection).
When the Rayleigh number is below the critical value for that fluid, heat transfer is primarily in the form of conduction; when it exceeds the critical value, heat transfer is primarily in the form of convection.
The Rayleigh number is defined as the product of the Grashof number, which describes the relationship between buoyancy and viscosity within a fluid, and the Prandtl number, which describes the relationship between momentum diffusivity and thermal diffusivity.
Hence the Rayleigh number itself may also be viewed as the ratio of buoyancy and viscosity forces times the ratio of momentum and thermal diffusivities.

## Slide 7: Forced vs Natural Convection
When analyzing potentially mixed convection, a parameter called the Archimedes number(Ar) parametrizes the relative strength of free and forced convection.
The Archimedes number is the ratio of Grashof number and the square of Reynolds number, which represents the ratio of buoyancy force and inertia force, and which stands in for the contribution of natural convection.
When Ar >> 1, natural convection dominates and when Ar << 1, forced convection dominates.

## Slide 8: Chapter 8 : Natural Convection
Natural convection over surfaces
1)
2)
3)
*C & n is depend on the geometry of the surface and flow regime.
n=1/4  laminar flow
n-=1/3  turbulent flow
*All the properties are evaluated at the film temperature, Tf=(Ts+T)/2
1. What is the difference between ReL and RaL ?
2. What is the transition range in a free convection boundary ?
(Laminar)
(Turbulent)

## Slide 9: Chapter 8 : Natural Convection
Transition in a free convection layer depends on the relative magnitude of the buoyancy and viscous forces
*The smooth and parallel lines in (a) indicate that the flow is laminar, whereas the eddies and irregularities in (b) indicate that the flow is turbulent.

## Slide 10: Chapter 8 : Natural Convection
General correlations for vertical plate
where,
Laminar | 104  RaL 109 | C = 0.59 | n = 1/4
Turbulent | 109  RaL 1013 | C = 0.10 | n = 1/3
For wide range and more accurate solution, use correlation Churchill and Chu
 Eq. (9.24)
 Eq. (9.26)
 Eq. (9.27)

## Slide 11: Chapter 8 : Natural Convection
For case of vertical cylinders, the previous Eqs. ( 9.24 to 9.27) are valid if the condition satisfied where
For case of inclined plates
In the case of a hot plate in a cooler environment, convection currents are weaker on the lower surface of the hot plate, and the rate of heat transfer is lower relative to the vertical plate case.
On the upper surface of a hot plate, the thickness of the boundary layer and thus the resistance to heat transfer decreases, and the rate of heat transfer increases relative to the vertical orientation.
In the case of a cold plate in a warmer environment, the opposite occurs.
Hot plate-cold env.
cold plate-hot env.

## Slide 12: Chapter 8 : Natural Convection
at the top and bottom surfaces of cooled and heated inclined plates, respectively, it is recommended that
Use equation 9.26
but replace g  g cos 
and only valid for 0    60

## Slide 13: Chapter 8 : Natural Convection
Example:
Consider a 0.6m x 0.6m thin square plate in a room at 30C. One side of the plate is maintained at a temperature of 90C, while the other side is insulated. Determine the rate of heat transfer from the plate by natural convection if the plate is vertical.

## Slide 14: Chapter 8 : Natural Convection

## Slide 15: Chapter 8 : Natural Convection

## Slide 16: Chapter 8 : Natural Convection
Example:
Consider a 0.6m x 0.6m thin square plate in a room at 30C. One side of the plate is maintained at a temperature of 90C, while the other side is insulated. Determine the rate of heat transfer from the plate by natural convection if the plate is
Vertical
Horizontal with hot surface facing up
Horizontal with hot surface facing down
Which position has the lowest heat transfer rate ? Why ?

## Slide 17: Chapter 8 : Natural Convection
The boundary layer over a hot horizontal cylinder starts to develop at the bottom, increasing in thickness along the circumference, and forming a rising plume at the top.
Therefore, the local Nusselt number is highest at the bottom, and lowest at the top of the cylinder when the boundary layer flow remains laminar.
The opposite is true in the case of a cold horizontal cylinder in a warmer medium, and the boundary layer in this case starts to develop at the top of the cylinder and ending with a descending plume at the bottom.

## Slide 18: Chapter 8 : Natural Convection
General correlations for an isothermal cylinder
where,
For wide range of Ra, use correlation Churchill and Chu
 Eq. (9.33)
 Eq. (9.34)

## Slide 19: Chapter 8 : Natural Convection
* Recommended when Pr  0.7 and RaD  1011
In case of isothermal sphere, general correlations is proposed by Churchill
Spheres
 Eq. (9.35)
In the limit as RaD → 0, Equation 9.35 reduces to NuD = 2, which corresponds to heat transfer by conduction between a spherical surface and a stationary infinite medium, as in Eqs. (7.48 & 7.49) – external convection for spherical object.

## Slide 20: Chapter 8 : Natural Convection
Problem 9.54:
A horizontal uninsulated steam pipe passes through a large room whose walls and ambient air are at 300K. The pipe of 150 mm diameter has an emissivity of 0.85 and an outer surface temperature of 400K. Calculate the heat loss per unit length from the pipe.
Schematic
Assumptions
Fluid properties
Analysis of total heat loss per unit length, q/L or q’
- Calculate RaD
- Calculate NuD
- Calculate hD
- finally, calculate total heat loss, q’
*If use Eq. 9.33, hD = 6.15 W/m2K
*If use Eq. 9.34, hD = 6.38 W/m2K
Within 4%

## Slide 24: Chapter 8 : Natural Convection
Characteristic length Lc: the distance between the hot and cold surfaces.
T1 and T2: the temperatures of the hot and cold surfaces.
Enclosures are frequently encountered in practice, and heat transfer through them is of practical interest.
Fluid properties at

## Slide 25: Chapter 8 : Natural Convection
- Flow is characterised by RaD value

## Slide 26: Chapter 8 : Natural Convection
Nu = 1

## Slide 27: Chapter 8 : Natural Convection
Selection will be determined by the value of RaL, Pr and aspect ratio H/L:

## Slide 28: Chapter 8 : Natural Convection
For larger aspect ratios, the following correlations have been proposed:

## Slide 29: Chapter 8 : Natural Convection
Example:
The vertical 0.8m high, 2m wide double pane window consists of two sheet of glass separated by a 2 cm air gap at atmospheric pressure. If the glass surface temperatures across the air gap are measured to be 12C and 2C, determine the rate of heat transfer through the window.
Schematic
Assumptions
Fluid properties at Tavg
Analysis of heat transfer
- Calculate RaD
- Calculate NuD
- Calculate h
- finally, calculate heat transfer

## Slide 30: Chapter 8 : Natural Convection
FC – forced convection
NC – natural convection