## Slide 1: Chapter 11 : Radiation Exchange between Surfaces
Define view factor and understand its importance in radiation heat transfer calculations.
Develop view factor relations and calculate the unknown view factors in an enclosure by using these relations.
Calculate radiation heat transfer between black surfaces.
Determine radiation heat transfer between diffuse and gray surfaces in an enclosure using the concept of radiosity.

## Slide 2: Chapter 11 : Radiation Exchange between Surfaces
11.1 The View Factor (also known as Configuration or Shape Factor)
View factor is a purely geometric quantity and is independent of the surface properties and temperature.
The view factor based on the assumption that the surfaces are diffuse emitters and diffuse reflectors is called the diffuse view factor, and the view factor based on the assumption that the surfaces are diffuse emitters but specular reflectors is called the specular view factor.
The view factor, Fi,j is a geometrical quantity corresponding to the fraction of the radiation leaving surface i that is intercepted by surface j.

## Slide 3: Chapter 11 : Radiation Exchange between Surfaces
11.1 The View Factor (also Configuration or Shape Factor)
The view factor integral provides a general expression for Fi,j .Consider exchange between differential areas dAi and dAj
 Eq.(13.1)
Fij is the fraction of the radiation leaving surface i that strikes surface j directly.
The view factor ranges between 0 and 1.

## Slide 4: Chapter 11 : Radiation Exchange between Surfaces
11.2 View factor relation
Reciprocity Relation.
Summation Rule for Enclosures. For N surfaces in the enclosure:
- It allows the calculations of a view factor from a knowledge of the other. Using Eqs. 13.1 & 13.2
 Eq.(13.3)
 Eq.(13.4)

## Slide 6: Chapter 11 : Radiation Exchange between Surfaces
 View factors for the enclosure formed by two spheres
The view factor has proven to be very useful in radiation analysis because it allows us to express the fraction of radiation leaving a surface that strikes another surface in terms of the orientation of these two surfaces relative to each other.
View factors of common geometries are evaluated and the results are given in analytical, graphical, and tabular form (Refer Tables 13.1 & 13.2, Figures 13.4, 13.5 & 13.6)

## Slide 12: Chapter 11 : Radiation Exchange between Surfaces
Problem 13.1:
Determine F12 and F21 for the following configurations:
Long duct. What is F22 for this case ?
h) Long concentric cylinders (D2 = 3D1)

## Slide 13: Chapter 11 : Radiation Exchange between Surfaces
11.3 Blackbody radiation exchange
When the surfaces involved can be approximated as blackbodies because of the absence of reflection, the net rate of radiation heat transfer from surface 1 to surface 2 is
Two general black surfaces maintained at uniform temperatures T1 and T2.
*Using term of reciprocity relation and emissive power
*A negative value for Q1 → 2 indicates that net radiation heat transfer is from surface 2 to surface 1.

## Slide 14: Chapter 11 : Radiation Exchange between Surfaces
Hence, the net radiation heat transfer from any surface i of an N surface enclosure is,
 Eq.(13.17)

## Slide 15: Chapter 11 : Radiation Exchange between Surfaces
Problem 13.19:
Consider the arrangement of the three black surfaces shown, where A1 = 0.05 m2 .
Determine the value of F13.
Calculate the net radiation heat transfer from A1 to A3, T1 = 1000 K and T3 = 500 K

## Slide 16: Chapter 11 : Radiation Exchange between Surfaces
11.4 Radiation exchange in real surfaces; diffuse, gray surfaces
Most enclosures encountered in practice involve nonblack surfaces, which allow multiple reflections to occur.
Radiation analysis of such enclosures becomes very complicated unless some simplifying assumptions are made.
It is common to assume the surfaces of an enclosure to be opaque, diffuse, and gray.
Also, each surface of the enclosure is isothermal, and both the incoming and outgoing radiation are uniform over each surface.

## Slide 17: Chapter 11 : Radiation Exchange between Surfaces
11.4 Radiation exchange in real surfaces; diffuse, gray surfaces
Radiosity
Radiosity, J: The total radiation energy leaving a surface per unit time and per unit area (emitted and reflected).
*For a surface i that is gray and opaque
(i = i and i + i = 1)
*recall about the radiosity term in Chapter10
For a blackbody  = 1
 Eq.(13.12)
Radiation Heat Transfer from a Surface:

## Slide 18: Chapter 11 : Radiation Exchange between Surfaces
11.4 Radiation exchange in real surfaces; diffuse, gray surfaces
Net Radiation Heat Transfer to or from a Surface
 The net rate of radiation heat transfer from a surface i
where,
= Surface resistance to radiation
*Electrical analogy of surface resistance to radiation
 Eq.(13.13)

## Slide 19: Chapter 11 : Radiation Exchange between Surfaces
11.4 Radiation exchange in real surfaces; diffuse, gray surfaces
Net Radiation Heat Transfer Between Any Two Surfaces
The net rate of radiation heat transfer from surface i to surface j is
*Apply the reciprocity relation
= Space resistance to radiation
where,
 Eq.(13.16)
*Electrical analogy of space resistance to radiation

## Slide 20: Chapter 11 : Radiation Exchange between Surfaces
11.5 Radiation exchange in an enclosure (two-surface enclosures)
a) Schematic of two-surface enclosure
b) Thermal network representation
Since there are only two surfaces (at different T), the net radiation:
*This important result is applicable to any two gray, diffuse, and opaque surfaces that form an enclosure. Other cases are summarized in Table 13.3
 Eq.(13.18)
 Figure 13.10

## Slide 22: Chapter 11 : Radiation Exchange between Surfaces
Problem 13.53
Two concentric spheres of diameter D1 = 0.8 m and D2 = 1.2 m are separated by an air space are separated by an air space and have surface temperatures of T1 = 400 K and T2 = 300K.
If the surfaces are black, what is the net rate of radiation exchange between the spheres ?
What is the net rate of radiation exchange between the surfaces if they are diffuse and gray with 1 = 0.5 and 2 = 0.05 ?
For case in (b), determine the convection heat transfer rate at the outer surface of outer sphere if the spheres is located in a surrounding where the temperature is 20C. Take the emissivity of the outer surface is 0.3