## Slide 1: Thermodynamics I Chapter 3 Energy, Heat and Work
Mohsin Mohd Sies
Fakulti Kejuruteraan Mekanikal, Universiti Teknologi Malaysia

## Slide 2: Energy, Heat and Work (Motivation)
A system changes due to interaction with its surroundings.
Energy interaction is a major factor.
This chapter studies the nature of energy and its various forms and transfers so that we are able to follow its interaction with a system.

## Slide 3
ENERGY & THE 1st LAW OF THERMO.
1st Law : concerning quantity of energy
Energy is conserved
(Amount of energy is constant, but can change forms)
(e.g. potential, kinetic, electrical, chemical, etc.)

## Slide 4
Energy
Macroscopic – system energy which value depends on a reference point (Kinetic Energy (KE), Potential Energy (PE)
Microscopic – energy due to molecular interactions & activity (independent of any reference point) (Internal Energy, U)
Total System Energy

## Slide 5
Kinetic Energy (KE)
Potential Energy (PE)

## Slide 6
Internal Energy, U
Molecular movement (vibration, collision, etc) sensible energy (molecular activity temperature)
Bond Energy between molecules (phase change) latent energy (constant temperature)
Bond Energy between atoms in a molecule chemical energy
Bond Energy between protons & neutrons in the nucleus nuclear energy

## Slide 7
Modes of Energy Transfer
Energy Interaction between System and Surrounding
Energy can cross the boundary (transferred) of a closed system by 2 methods;
HEAT & WORK

## Slide 8
HEAT, Q [J, kJ]
Heat - Energy that is being transferred due to a temperature difference
Heat is a mode of energy transfer
Heat is not a property
Energy is related to states (property) Heat is related to processes (not a property, depends on the path)
= rate of heat transfer
Amount of heat transferred during a process (depends on the path)

## Slide 9
Heat (ctd.)
system
Qin= +ve
Qout= -ve
Adiabatic Process (Q = 0)
insulated
Tsystem = Tsurrounding
Adiabatic ≠ Isothermal!
(T can change by other methods; energy can enter system by work)

## Slide 10
WORK, W [J, kJ]
Work -–Energy that is crossing the boundary other than heat
(electrical, stirrer, shaft, moving piston, etc.)
Not a property (related to process)
Mode of energy transfer
Win= -ve
Wout= +ve
system
= rate of work = power
Depends on path

## Slide 11
Types of Work
Work
Electrical
Mechanical
Boundary
Gravitational
Acceleration
Shaft
Spring

## Slide 12
Boundary Work for Polytropic Processes
Boundary Work
General Polytropic Work
( n  1 )
Const. Pressure Work (n=0)
Isothermal Work (n=1) ideal gas
Const. Volume Work (dv=0)
Area under P-v graph

## Slide 13
1st Law Closed System
Qin
Qout
Win
Wout
Net total energy transfer in the form of heat and work
Net change of system energy

## Slide 14
Q – W = U + KE + PE
Net transfer of energy
Energy storage in different modes
Esystem= U + KE + PE
Esystem= U + KE + PE
- Recall that System Energy consists of:
or
thus;
Q – W = Esystem= U + KE + PE
Or can be called as the 1st Law/Energy Balance of a Closed System;

## Slide 15
Q – W = U + KE + PE [kJ]
1st Law for Closed System in different forms;
q – w = u + ke + pe [kJ/kg]
per unit mass;
Rate form;
[kW]
Cyclic Process E =0

## Slide 16
summary;
Q – W = U + KE + PE
mg(z2-z1)
m(u2-u1) water (Table)
mCv(T2-T1) ideal gas
Electrical
Mechanical
  Boundary
  etc…